CONCEPTS YOU SHOULD UNDERSTAND:

- Time of propagation, tp

- Velocity of propagation, vp , u

- Frequency - sinusoidal, f

- Spatial frequency - sinusoidal, (

- Period - sinusoidal, T

- Wavelength - sinusoidal, (

- Attenuation constant, (

- Forward/positive propagation, reverse/backward propagation – sinusoidal and transient

- Stand wave pattern/envelope - sinusoidal

- Standing wave ratio - sinusoidal, SWR

- Pulse width – transient

- Line length/Electrical length – sinusoidal

- Line length vs. pulse width – transient

- Source impedance, Zs

- Load impedance, Zl

- Line impedance, Zo

- Input impedance - sinusoidal, Zin

- Phasor notation – sinusoidal

- Time domain notation – sinusoidal

- Understand the relationship between lumped parameters and transmission lines

- Lumped parameter values, l, c, r and g

- Pulse amplitudes, V1+, V1-, V2+, V2-, …

PROBLEMS YOU SHOULD KNOW HOW TO DO

- Determine the relationship between inductance, capacitance and characteristic impedance

- Determine the relationship between inductance, capacitance and velocity

- Determine the complete expression of a wave from a voltage vs. time plot

- Determine the reflection coefficient from both the source and the load

- Determine the standing wave pattern for both voltage and current on a finite length of transmission line

- Determine the standing wave pattern for both voltage and current on an infinite length of transmission line

- Determine the location of maxima and minima of the standing wave pattern

- Determine the input impedance of a finite length of line

- Determine the input impedance for a short circuit load

- Determine the input impedance for an open circuit load

- Determine the effective load at a transmission line junction

- Determine both the voltage and current wave expressions in phasor and time domain notation

- Determine the complex amplitude for both the forward and backward traveling waves

- Determine the total voltage and current on a line

- Determine the voltage at the input and output of a transmission line for a pulse with a pulse width much shorter than the time of propagation

- Determine the voltage at the input and output of a transmission line for a pulse with a pulse width much longer than the time of propagation