PREPARATION ASSIGNMENTS-2

Due Monday, January 26

1. Consider a TV antenna lead-in wire of length l=15 cm having a characteristic impedance of Z0=200 Ω and nothing connected at its end (i.e. open circuit). Find the input impedance of the line if it is to be used at 300 MHz.

Due Wednesday, January 28

- An open wire (air insulated) telephone line consists of two parallel lines made of copper with diameters 0.25 mm and spaced 25 cm apart. Determine

a) The propagation constant γ

b) Its real and imaginary parts α and β

c) The characteristic impedance Z0.

Assume that the operation frequency is 1.5 kHz.

Due Thursday, January 29

1.  A 70 Ω high frequency lossless line is used at a frequency where λ=80 cm with a load of 140+j90 [Ω] at z=0. Use the Smith Chart to find:

- Reflection coefficient, Γ

- SWR (standing wave ratio) , S

- Distance to the first voltage maximum from the load

- Distance to the first voltage minimum from the load

- The impedance at voltage maximum

- The impedance at voltage minimum

Include your Smith Chart drawings to your answers.

Due Monday, February 2

Generate a bounce diagram for the voltage V(z,t) for a 1.5 m long lossless line characterized  by Z0 and up=2c/3 (where c is the velocity of the light) if the line is fed by a step voltage applied at t=0  by a generator circuit with Vg= 60 V and Rg=4Z0 [Ω]. The line is terminated with a load ZL=9Z0.

Use your bounce diagram to plot the voltage variation with time at z=0.75 m.

Due Wednesday, February 4

Do the following indefinite integrals:

(spherical coordinates)

(cylindrical coordinates)

(cylindrical coordinates)

(cylindrical coordinates)

(spherical coordinates)

Do the following definite integrals:

(spherical coordinates)

(cylindrical coordinates)

(spherical coordinates)