| components | Resistors | Capacitors | Inductors |
| --- | --- | --- | --- |
| symbol | R | C | L |
| general equation |  |  |  |
| combining in series | RT = R1 + R2 + ... + Rn |  | LT = L1 + L2 + ... + Ln |
| combining in parallel |  | CT = C1 + C2 + ... + Cn |  |
| impedance |  |  |  |
| frequency(0 | R | open circuit | short circuit |
| frequency(∞ | R | short circuit | open circuit |

| Laws and Rules |
| --- |
| Ohm’s Law | V = IR VT = ITRT |
| Kirchoff’s Voltage Law | Sum of voltages in a loop is zero. |
| Kirchoff’s Current Law | Sum of currents entering junction equals the sum of currents leaving junction. |
| Reading Resistors | XYZ = XY x 10Z ohms | black-brown-R-O-Y-G-B-V-grey-white 0 1 2 3 4 5 6 7 8 9 |
| Reading Capacitors | XYZ = XY x 10Z picofarads = XY x 10(Z - 6) microfarads |
| Logarithmic Scales | log(f)=[decade]([percent across] | f = 10[decade].[percent across] |
| suffixes | K (103) Meg(106) G(109) T(1012) | m(10-3) ((10-6) n(10-9) p(10-12) |
| Euler’s Identity | parallel combination shortcut | Power Equation |

| Voltage Dividers | Sine Waves |
| --- | --- |

| Transformers |
| --- |
|  | ideal equations | input impedance |

| Calculating Inductance | Calculating Resistance |
| --- | --- |
| Long Coil | Ring shaped Coil |  |

| Complex Polar Coordinates |
| --- |
| Complex numbers: (, 1/j = -j ) Polar to Cartesian transform: , Cartesian to Polar transform: | phases 0 -A or -( jA -jA tan-1(1) or - tan-1(-1) - or x+jy tan-1(y/x) where A is a constant |

| Transfer Functions |
| --- |
| Combining Impedances | series | parallel |
| Low Frequency Approximation |  |
| High Frequency Approximation |  |
| Using Transfer Functions |  |  |

| Filters |
| --- |
| RC Circuit (corner) | RL Circuit (corner) | RLC Circuit (resonant) |