Homework 4

Charge Distribution

1.

The radially dependent volume charge density ρv=3r2  [C/m3] exists within a sphere of radius r=3 cm. Find the total charge Q contained by that sphere.

Gauss’s Law

2.   A long cylinder of radius 0.05 meters has a volume charge density which is proportional to the distance from the axis, ρv=0.05r. Find the vector electric field inside the cylinder using Gauss’ Law in integral form. Show the Gaussian surface and the electric field direction.

z

3. Use the spreadsheet method for solving Laplace’s equation  to find the capacitance of the object we solved in class.  The dielectric constant is 5.0  The geometry  is illustrated below:

# Text boxes

2.0 cm

4.0 cm

Flux Lines

1.0 cm

V=0

V=2000

5.0 cm