Fields and Waves I

Fall 2007

# Homework 6

- For the core below we have voltage source connected to the primary winding (N1 turns) producing a sinusoidal voltage.  The secondary winding (N2 turns) is open circuited. The cross- sectional area is .  The core length is  The flux density in the core is There are N1 = 100 turns in the primary  coil and N2 =300 turns in the secondary.  Ignore the resistance in the windings. .

A) Find the applied voltage to the primary and the open circuit voltage on the secondary..

B)  We now connect a load to the secondary (N2) of 50 Ohms resistance. Find the current in the primary and secondary  windings.

N2

N1

2. A Flux density is increasing as B = 0.1t Tesla through a loop of area 1 square meter.  The loop has 2 resistors as shown below.  There are 3 volt meters attached. What is the reading of each volt meter?

3. A rectangular loop 10 cm by 10 cm is coplanar with a long wire with current I = 2.5cos(2π*104t) Amps.  The resistance of the loop is 20 Ohms and we can ignore the inductance.  Find the current circulating in the loop and the direction.

# Text boxes

B=0.1t Tesla

V2

V3

V1

5cm

I Amps

10 cm

10 cm