Homework 7

Fields and Waves I

# Fall 2005

1. A transformer core has a cross sectional area of 6 cm2.  We apply 60 Hertz voltage of 120 Volts RMS.  The core material saturates at 1.8 Tesla.  How many turns are required to keep the peak flux density under this value?

2. A coax cable has  and inner conductor radius  of 2.0 mm and outer conductor radius of 4.0 mm.  We apply a voltage of .  Find the displacement current per meter of length.  What would the conductivity of the insulation have to be in order to get the same displacement and conduction current.

3. A uniform plane wave is traveling in a media with and the frequency is 1.5 GHz.  Find

4. A wave is described at a fixed z position by  Describe the polarization of the electric field.