Homework 3

Due 18 February 2004

Charge Distribution

1. Finding total charge

a) The radially dependent volume charge density ρv=50r2  [C/m3] exists within a sphere of radius r=5 cm. Find the total charge Q contained by that sphere.

b) The same sphere is now covered with the angularly dependent surface charge density ρs=0.002cos2θ  [C/m2].  Find the total charge Q on the spherical surface.

Gauss’s Law

2.   A long cylinder carries a volume charge density which is proportional to the distance from the axis, ρv= 5r. Find the vector electric field inside the cylinder using Gauss’ Law in integral form. Show the Gaussian surface and the electric field direction.

z

3.  	A total charge Q is enclosed in a cube 2m on a side, located in the first octant with three of its sides coincident with x,y,z axes and one of its corners is at the origin (see the figure). The electric flux density in this region is: D= xy2z3 (C/m2)

- Apply Gauss’ law in integral form to obtain the total charge in the cube

- Find the volume charge density ρv for the cube from D.

- Find the total charge Q enclosed in the cube using the volume charge density ρv (Note—your answers to parts a and c should agree.)

Electric Field and Potential

- A circular ring of charge of radius a lies in the x-y plane and is centered at the origin. If the ring is in air and carries a uniform density ρl ,

  - Find the electrical potential at (0,0,z)

  - Find the corresponding vector electric field E(0,0,z)

- A square in the x-y plane in free space has a point charge of +Q at corner (a/2,a/2) and the same at corner (a/2, -a/2) and a point charge of –Q at each of the other two corners.

  - Find the electric potential at any point P along the x axis.

  - Evaluate V at x=a/2

# Text boxes

2

2

2

x

y

z