Homework 5

Fields and Waves I

Fall 2004

For the figure below the top conductor is at 100 Volts and the bottom conductor is at 0 Volts.  Use a spreadsheet (finite difference iterations) to solve Laplace’s equation.  Assume 1 meter depth and that the material is vacuum.  Find the capacitance per meter depth.. The spacing

For the coaxial cable, we have a gas insulation () with the center conductor of radius a supported by 3 solid spacers ().  The outer conductor has a radius b. The solid spacers take up a total of . If the potential difference between the inner and outer conductors is , find the electric field, flux density and potential everywhere.  Find the capacitance per unit depth.  Explain how the interface conditions are satisfied

.

# Text boxes

spacer

Flux Lines

V=0

V=100