PREPARATION ASSIGNMENTS-4

Due Monday, February 23

- a) Find the electric potential at point P which is 5 cm from a positive point charge of 40 nC in air?

b) Solve the problem for a medium of relative permittivity 3.

c) What is the work required to move a +8 nC charge from infinity to point P? (in   	    air)

Due Thursday, February 26

- a) Calculate the conductivity of a 4 mm diameter, 5 m long wire if its measured resistance is 12 mΩ?

b) What is the material of the wire?

2.  When is a dielectric medium said to be “homogeneous, linear and isotropic”?

Due Monday, March 1

1. By using the above figure and the boundary conditions between two dielectric   	media, find E1 if E2 = [V/m] and  ε1=2ε0, ε2=4ε0  for

a) the boundary with no charge

b) the boundary with surface charge density ρs=3.5e-11 [C/m2].

Due Wednesday, March 3

- In a dielectric medium with εr=5, the electric field is given by

E=  [V/m]. Calculate the electrostatic energy stored     	in the region -1m ≤x≤1 m, 0≤y≤2 m, 0≤z≤3 m.