Question 1)  Flip Flops and Counters (25 points)

- Fill in the truth table for a JK flip flop. Use Q0 or to denote the previous value of Q and . (4 pts)

| J | K | CLK | Q |  |
| --- | --- | --- | --- | --- |

b) Fill in the following table which describes the output of the counter.  Assume that the clock column gives the number of pulses since time 0 and QA, QB, QC and QD are the counter outputs.  The initial state is given. (5 points)

| Clock Pulses | QA | QB | QC | QD |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |

c) When the  pin on the JK flip flop goes to 0 what happens to Q and ? Why is this pin necessary? (3 points)

d) Both the JK flip flop and the 74393 counter are edge-triggered. What does this mean? Why is edge triggering useful? (4 points)

e) In Figure 1a we show a counter connected to the inputs of a JK flip flop. Draw the output versus time at each of the points specified in the diagram below. Assume that initially both the counter and the JK flip flop are cleared at time t=0.  Note that since both the counter and the flip flop trigger on the falling edge of the clock, we have added an inverter to one of them to prevent race conditions. (9 pts)

Question 2) NAND Gate Circuit (25 points)

Below is a picture of a series of NAND gates hooked together to form one of the basic gates we have studied and the PSpice output for the circuit.

a) Fill in the truth table for the circuit (6 pts).

| A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- |

b) What gate does this represent (2 pts)?

c) Write a boolean expression for this circuit.  Do not simplify. (5 pts).

d) Use the Boolean Algebra Rules below to simplify the expression and prove that this circuit is the gate you have indicated (12 pts).

Note that the NOT operation is indicated here by ~ instead of as a bar over the letter.

You are free to use either notation.  You can indicate the rule by the letter.

Question 3)  Combinational Logic (15 points)

Draw the truth table for the circuit above:

| A | B | C | D | E | F | G | H | I | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Question 4) Digital-to-Analog Converter (20 points)

The circuit below is a “Voltage Adder” followed by an “Inverting Op-Amp”, that converts digital signals into analog signals.  This circuit produces an analog output voltage equal to the binary word ABCD in terms of the four inputs.  Please assume that the input voltage levels for this circuit is 5 Volts for a logic of “one” and 0 Volts for a logic “zero” and that R5 = 10K, R6 = 5K and R7 = 10K.

a) Select values for R1, R2, R3, and R4 so that the output voltage will be the decimal equivalent of ABCD.  For example, if ABCD=1010, or equivalently VA=VC=5 V, VB=VD=0 V, then Vout = 10 V. The circuit should work for all possible ABCD combinations. (12 points)

# R1 =	 		R2 =			R3 =	 			R4 =

b) Show that your selection of resistors above is correct by comparing the calculated Vout with the a digital input of 1101 (4 points)

c) Show that your selection of resistors above is correct by comparing the calculated Vout with the a digital input of 1011 (4 points)

Question 5)  Transistors  (15 points)

Figure 5b

- Redraw the circuit in Figure 5b when the voltage at Va and the voltage at Vb is 0V.  Draw the transistors as a switch either open or closed. (3 points)

- Redraw the circuit in Figure 5b when the voltage at Va and the voltage at Vb is 5V.  Draw the transistors as a switch either open or closed. (3 points)

- Fill in the following table of Vout as a function of Va and Vb based on the model you gave in part a and b. (4 points)

| Va | Vb | Vout |
| --- | --- | --- |
| 0V | 0V |  |
| 0V | 5V |  |
| 5V | 0V |  |
| 5V | 5V |  |

- What kind of gate is this? (5 points)

  - AND

  - NAND

  - OR

  - NOR

  - XOR

  - None of the above