# 1) 555 Timer (20pts)

# a)  What is the frequency of the 555 set at?  What are T1 and T2?  9pts

b)  Calculate R1 and R2.  8 pts

# c)  What is the current through R3 when the 555 timer when the 555 timer is “on”?  What is the current through R3 when the 555 timer is “off”? 3 pts

2) Inductance Measurement (20 points)

In the circuit below, Vin = 200mv, R2 = 300C1 = 0.05F and L1 is unknown.

Plot I: Displays an AC sweep of the voltage at points A and B.

Pot II:  Displays an AC sweep of the phase at points A and B.

a) Find the transfer function, H(j), at point B.  Determine the function and the magnitude and the phase at high and low frequencies.

(2 pts) H(j) =

(1 pt) H(jlo) =				(1 pt) H(jhi) =

(1 pt) | H(jlo) | =				(1 pt) | H(jhi) | =

(1 pt) (H(jlo) =				(1 pt) (H(jhi) =

b) Based on your results from part a), indicate on plot I the trace for the magnitude of the voltage at point B (2 pts).

c) Based on your results from part a), indicate on plot II the trace for the phase at point B (2 pts).

d) Find the resonance frequency f0 from the plot. Notice that the x-axis has logarithmic scale. (ie. 100.5 = 3.16) (2 pts)

e) Solve for the unknown inductance. (6 pts)

3) Zener Diodes (20 pts)

a) Which of the three plots on the following page matches this circuit diagram at points A and B. (7pt)     Show your work.

# B)

i. What is the current through R4 when the AC voltage is at +10 volts and the value of R4 is 50,000 ohms? 5000 ohms? 50 ohms? (6pt)

ii. Below are 3 graphs that match 3 values for R4.  Choose which goes with 50 ohms, 5000 ohms and 50000 ohms (7 pnts)

4) Op-Amp Configurations (20 points)

a) Seven circuits are shown below. (Connections to power supply are not displayed but assumed).  For each circuit, identify the function (1 pnt each) and give the mathematical relationship that relates the input and output voltages (1 pnt each).

1.

2.

3.

4.

5.

6.

7.

b) Consider the following input plot:

If this was used as the input to the circuit in 1 of this question, sketch what the graph of the output would be.  Make sure the frequency and the amplitude and the value at 0 seconds are clearly indicated.  Assume C1=1 nF and R1=1 K ohms.  Show your work.

5)  Circuit Functionality (20 pts)

Below is a graph of the input and output, just to give you some reference of what the circuit will do.  The source is 1V at 10KHz.

List the functionality of each block, A,B,C,D and E.  (4 pt each)