1. Resistive Circuits (20 points)

a) Given the circuit above, calculate the DC offset voltage at point A. (5 points)

b) For the same circuit, calculate the amplitude of the voltage at point A. (5 points)

c) What is the current through R1? (5 points)

c) Which of the following plots corresponds to the correct output for the circuit pictured above?  (5 points)

2. Thevenin Circuits (20 points)

Let V2=12V, R1=50 ohms, R2=1K ohms, R3=2K ohms, and R4=500 ohms.

- Find the Thevenin voltage between A and B (8 points)

- Find the Thevenin resistance (8 points)

- Draw the Thevenin equivalent circuit with a load of 4K ohms. (4 points)

3. Sinusoids (20 points)

The following data was obtained for some kind of a measurement.

The horizontal scale is in days. The vertical scale is unknown at the moment.

a) Since this data looks approximately sinusoidal, determine its period and frequency. You may make any reasonable assumption.

b) The data is not exactly sinusoidal since it is very noisy and also the maximums and minimums are not the same. In addition, there is a finite offset (DC) value. What is the approximate value of the offset?

c) Write a mathematical expression for the signal and its offset.

d) Based on your answer to part (a) and the values given for the data, what do you suppose is being measured?

4. Inductors and Capacitors at High and Low Frequency (20 points)

a) The circuit shown below is a delay line. That is, for some signals input at terminals A and B, the same signals will appear at terminals C and D, but delayed in time.

i) Simplify this circuit for zero frequency (DC) conditions (4 points)

ii)  Simplify this circuit for very, very high frequencies (4 points)

iii) Given that no other components are connected to A&B or C&D, what is the resistance that would be measured at very low and infinite frequency at both sets of terminals? (8 points)

Assume R1=R2=R3=R4=R5=R6=2K ohms, C1=C2=C3=1F, and L1=L2=L3=3mH

Very Low Frequencies				Very High Frequencies

RAB =							RAB =

RCD=							RCD=

b) Many of you own devices that connect to your computers that have a thick cylindrical section that surrounds one of the power or signal cords. This is a magnetic material that adds inductance to both signal leads. The resulting circuit looks like the following.

Simplify this circuit at high and low frequencies. (4 points)

# 5. Instrumentation and Sine Waves (20 points)

a)  Explain as simply as possible how to set up the function generator and ‘scope to display the signal shown. (Use of Autoscale is NOT allowed).  Give specific values.

(8 points)

b) If you were to attach another function generator to channel 2 of the ‘scope, what would you set the frequency of the signal output by the second function generator to in order to generate a Lissajous pattern that looks like an upright figure eight? (Assume channel 1 is on the x axis) (2 points)

How would you set up the ‘scope to display this signal? (2 points)

c) When the function generator is connected to the scope you should notice a discrepancy between the reading on the display panel of the function generator, and the signal displayed on the scope.  What discrepancy do you see and which device is correct?

# (2 points)

# Why? (6 points)