Question 1 -- Astable Multivibrator

The circuit above has been simulated using PSpice.  Using PROBE, the voltages at pins 2, 6, 7, and 3 have been displayed.

a. Label which trace goes with which pin (2,3,6,7) in each time period. Be sure that you label the traces in both the on and off parts of the pulse cycle. (8 points)

b. What if the duty cycle of the pulses in the plot? (4 points)

b. Determine the values of R1 and R2 from the information in this plot.  (4 points)

c.  What could you do to increase the duty cycle of the pulses? (4 points)

Question 2 – Measuring Inductance (20 points)

Given the following circuit and its AC sweep below:

a) Find the transfer function, H(j), at point B.  Determine the function and the magnitude and the phase at high and low frequencies. (8 points)

(2 pts) H(j) =

(1 pt) H(jlo) =				(1 pt) H(jhi) =

(1 pt) | H(jlo) | =				(1 pt) | H(jhi) | =

(1 pt) (H(jlo) =				(1 pt) (H(jhi) =

b) Based on your results from part a), indicate on the plot the trace for the magnitude of the voltage at point B (2 points).

c) Find the resonant frequency f0 from the plot. Notice that the x-axis has logarithmic scale. (ie. 100.5 = 3.16) (3 points)

d) Solve for the unknown inductance. (5 points)

e) Both of the resistances in this circuit are not physical resistors.  They represent the resistance of something else in the circuit.  Assuming that these do not represent wire resistance, what do they represent? (2 points)

Question 3 -- Op Amp Differentiator (20 points)

Given: C1=0.001 F  R2= 500

In this question, we will look at the effect of the 50 ohm input resistance on the op-amp differentiator.

- What is the expression for Vout/Vin for circuit A above.  Give this in terms of C1, R2, j and . (3 points)

b) Determine the expression for Vout/Vin for circuit B above.  (Be sure to include the impedance of the function generator, R1.)  Give this in terms of C1, R1, R2, j and . (3 points)

c) Find the corner frequency fc for circuit B.  This should be a numerical value in Hertz. (4 points)

d) Does circuit B behave like circuit A above or below the corner frequency?  Use limits to show how you know this. (6 points)

e)  At about what frequencies does the 50 ohm impedance of the function generator prevent this circuit from differentiating?  (4 points)

Question 4 – Zener Diodes (20 points)

The circuit above is a zener diode voltage regulator.  Assume the zener voltage of the diode is 4.7 volts and its forward bias voltage is 0.7 volts.

1) What does a voltage regulator do? (2 points)

2) What would the voltage at V2 be when V1 = 6V if R2 has the following values:

(6 points)

i) 1K ohms

ii) 10K ohms

iii) 100K ohms

3) What would the voltage at V2 be when V1 = -6V and if R2 has the following values: (6 points)

i) 1K ohms

ii) 10K ohms

iii) 100K ohms

3) Each of the following three plots was made with a different value for R2: 1K ohms, 10K ohms and 100K ohms.  Indicate which plot was made with which value for R2.

(6 points)

Question 5 -- Circuit functionality and transformers (20 points)

The following circuit was constructed to test two DC power supplies. One is a battery and one is a wall wart (connects to a normal 120V outlet). The boxes surrounding each part of the circuit identify the functional blocks (each has a specific purpose). Each of the boxes is also shown expanded for clarity.

a. Identify the function of each of the nine blocks. (Draw a line to connect the letter of the block to its function). (9 points)

A			1.   Measure output voltage

B			2.   Rectify AC voltage

C			3.   Input signal voltage

D			4.   Block DC voltage while passing AC voltage

E			5.   Smooth ripples to improve DC output voltage

F			6.   Step AC voltage down from 120V to 12V

G			7.   Provide AC power for DC supply

H			8.   Amplify signal voltage

I			9.   –12V power supply

b. On the next page are plotted six voltages measured at various points in the circuit. Identify each of the voltages by indicating the block for which this is the output voltage. Note that there are only six voltages but there are eight output points for the blocks. (6 points)

c. Based on the voltages you have just identified, what is the ratio of the input voltage to the output voltage of the transformer? Note that a real transformer is modeled here so that it has finite resistance in its windings. However, you can neglect these small resistances in the rest of this problem. (3 points)

d. If the primary winding of the transformer has 10000 turns, how many turns does the secondary winding have to produce this change in voltage? (2 points)