Question 1) NAND Gate Circuit (15 points)

Below is a picture of a series of NAND gates hooked together to form one of the basic gates we have studied and the PSpice output for the circuit

- Fill in the truth table for the circuit ( 9 pts)

| A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- |

- What gate does this represent (2 pts)?

- Write a boolean expression for this circuit. Do not simplify. (4 pts)

Question 2) Schmitt Trigger Model

Below is a Schmitt trigger circuit connected to a switch. The plot below the circuit is the PSpice output from this circuit

- Indicate the voltage at node “A” and node “B” on the output plot below (4 pts)

- Estimate the value of the hysteresis for the Schmitt trigger model AND indicate the hysteresis range on the output plot (8 pts)

- What is the saturation voltage range of the op-amp in the model? (4 pts)

- What is the operating region of the transistor in region 1 (Sat, active, OFF)? What is the current in the transistor in “region 1” (4 pts)

- What is the operating region of the transistor in region 2 (Sat, active, OFF)? What is the current in the transistor in “region 1” (4 pts)

# Text boxes

Region 1

Region 2