3. Schmitt Trigger

The following circuit was configured to study Schmitt Triggers. It includes the Schmitt trigger device (7414) we studied in Experiment 10 and the op-amp configuration assembled to produce a Schmitt Trigger circuit.

The voltage source is a combination of two sources at two sources – one is sinusoidal and one is a triangular wave The latter source has the higher frequency. The voltage levels for the op-amp Schmitt Trigger circuit are higher than for the commercial Schmitt Trigger. Thus, two resistors and a voltage source are used to change the input voltages to levels appropriate for a logic circuit.  Note that we are also operating the op-amp in an unbalanced mode with the negative voltage source set to zero.

The voltage signals measured at points A, B, C, & D in the circuit look like:

The voltage scale on the bottom plot ranges from -5 to 10 Volts, while the scale on the top plot varies from -2 to 4 Volts.

- Label each of the four signals with the letter A, B, C, or D indicating where it is measured.

- What are the frequencies for both sources?  The sinusoidal source operates at 800Hz. The triangular wave source has a frequency of 20kHz.

- At what voltages do the two circuits switch output states?  For the top plot, the output goes high at an input of .9V and goes back low at 1.7V. (These are consistent with the typical values quoted in the TI spec sheet. For the bottom plot the output goes high at 2.13V and low at 4.87V. Note that acceptable voltages can be within 0.3V of these values for the bottom plot and .2V for the top plot. However, careful reading of the plots at the point where the voltage switches, should give these values. See an expanded version of the bottom plot on the next page.

- Assuming, as is shown, that R2 = 10k Ohms, what must the value of R3 be to cause the output measured across R4 to switch at these voltages? For the case where the output is high (8.6V) the switch point is 4.87=(10k/(R3+10k))*3+(R3/(R3+10k))*8.6 and where the output is low (.4V) the switch point is 2.13=3*(10k/(R3+10k))+(R3/(10k+R3))*.4. Solving these two expressions gives R3 about 5k. Reading the numbers less accurately off of the graph will result in two different answers, but both should be near 5k.  Given the range of voltages, any value from 4k to 6k is fine.

Expanded version of lower plot

# Text boxes

Voltage source with one AC Signal and one triangular wave signal

Modifies the voltage source to appropriate levels for Schmitt Trigger

A

B

C

D

A

B

C

D