3. Schmitt Trigger

The following circuit was configured to study Schmitt Triggers. It includes the Schmitt trigger device (7414) we studied in Experiment 10 and the op-amp configuration assembled to produce a Schmitt Trigger circuit.

The voltage source is a combination of two sources at two sources – one is sinusoidal and one is a triangular wave The latter source has the higher frequency. The voltage levels for the op-amp Schmitt Trigger circuit are higher than for the commercial Schmitt Trigger. Thus, two resistors and a voltage source are used to change the input voltages to levels appropriate for a logic circuit.  Note that we are also operating the op-amp in an unbalanced mode with the negative voltage source set to zero.

The voltage signals measured at points A, B, C, & D in the circuit look like:

The voltage scale on the bottom plot ranges from -5 to 10 Volts, while the scale on the top plot varies from -2 to 4 Volts.

- Label each of the four signals with the letter A, B, C, or D indicating where it is measured.

- What are the frequencies for both sources?

- At what voltages do the two circuits switch output states?

- Assuming, as is shown, that R2 = 10k Ohms, what must the value of R3 be to cause the output measured across R4 to switch at these voltages?

# Text boxes

Voltage source with one AC Signal and one triangular wave signal

Modifies the voltage source to appropriate levels for Schmitt Trigger

A

B

C

D