Question 1 -- Flip Flops and Counters (20 points)

a) Complete the timing diagram for the circuit above.  Note that the first trace shown is DSTM1 (flip flop clock), the second trace shown is DSTM2 (counter clock), and DSTM3 provides an initial reset pulse to both of the devices.  You can assume that all outputs are initially 0 and that all three devices change on the falling edge of the clock..   Draw traces for all six of the points indicated: (J1, K1, Q1, J2, K2, Q2)

(3 points each = 18 points)

- To what value does the counter count in the time frame indicated? (2 points)

Question 2 – Logic Gates (20 points)

- Fill in the truth table for the circuit above: (12 points)

| A | B | C | D | E | F | G | H | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 |  |  |  |  |  |  |
| 0 | 0 | 1 |  |  |  |  |  |  |
| 0 | 1 | 0 |  |  |  |  |  |  |
| 0 | 1 | 1 |  |  |  |  |  |  |
| 1 | 0 | 0 |  |  |  |  |  |  |
| 1 | 0 | 1 |  |  |  |  |  |  |
| 1 | 1 | 0 |  |  |  |  |  |  |
| 1 | 1 | 1 |  |  |  |  |  |  |

b) Write the Boolean expression for the circuit in b.  Do not simplify. (6 points)

c) What type of gate could the above circuit be replaced with to give the same results for Q based on A, B and C? (2 points)

  - Three input and gate

  - Three input or gate

  - Three input nor gate

  - Three input nand gate

5) none of the above

Extra credit (1 point): Simplify the Boolean expression in b) using the rules of Boolean algebra on your crib sheet.

3. Schmitt Trigger

The following circuit was configured to study Schmitt Triggers. It includes the Schmitt trigger device (7414) we studied in Experiment 10 and the op-amp configuration assembled to produce a Schmitt Trigger circuit.

The voltage source is a combination of two sources – one is sinusoidal and one is a triangular wave The latter source has the higher frequency. The voltage levels for the op-amp Schmitt Trigger circuit are higher than for the commercial Schmitt Trigger. Thus, two resistors and a voltage source are used to change the input voltages to levels appropriate for a logic circuit.  Note that we are also operating the op-amp in an unbalanced mode with the negative voltage source set to zero.

The voltage signals measured at points A, B, C, & D in the circuit look like:

The voltage scale on the bottom plot ranges from -5 to 10 Volts, while the scale on the top plot varies from -2 to 4 Volts.

- Label each of the four signals with the letter A, B, C, or D indicating where it is measured. (4 points)

- What are the frequencies for both sources?  (4 points)

- At what voltages do the two circuits switch output states?  (8 points)

Top plot (Low to High):			Top plot (High to Low):

Bottom Plot (Low to High):		Bottom plot (High to Low):

- Assuming, as is shown, that R2 = 10k Ohms, what must the value of R3 be to cause the output measured across R4 to switch at these voltages? (4 points)

Question 4 -- Digital-to-Analog Converter (20 points)

For a computer or other digital device to interface with external analog circuits and devices, a digital-to-analog converter (DAC) is required.  The most common DAC is a R-2R resistor ladder network, which requires only two precision resistor values R and 2R.  A 4-bit R-2R resistor ladder network is shown below:

The digital input to the DAC is a 4-bit binary number represented by bits b0, b1, b2 and b3, where b0 is the least significant bit (LSB) and b3 is the most significant bit (MSB).  Each bit in the circuit controls a switch between ground and the inverting input op amp.  When a bit is 1, the corresponding switch is connected to the op-amp;  when a bit is zero, the corresponding switch is connected to ground.

a) If we assume this is an ideal op-amp, we can analyze the voltage levels in the circuit by removing it.  Below is a picture of the circuit when all bits are zero.  Determine the voltage levels at V0, V1, V2 and V3 in terms of the source voltage, Vs. (8 points)

b) What type of op-amp circuit is in this DAC? (1 point)

c) If we assume that closing each switch has negligible effect on the voltage levels from a), what will be the output of the DAC circuit, Vout (in terms of Vs), when the input

(b3 b2 b1 b0) is: (10 points)

0001:

0010:

0100:

1000:

1111: [Hint: Use principal of superposition.]

c) In terms of Vs, what is the range of the analog output for a 4 bit binary input? (ie.  If the input ranges from 0000 to 1111, what is the output range?) (1 point)

Question 5)  Transistors  (20 points)

- Redraw Figure 5a with the transistors modeled as switch and a diode. (4 points)

- Fill in the following table of C and D as a function of A and B based on the model you gave in part c. (6 points)

| A | B | C | D |
| --- | --- | --- | --- |
| 0V | 0V |  |  |
| 0V | 5V |  |  |
| 5V | 0V |  |  |
| 5V | 5V |  |  |

- If we assume the output of this gate is measured at D, what kind of gate is it? (5 points)

  - AND

  - NAND

  - OR

  - NOR

  - XOR

  - None of the above

# Text boxes

A

Modifies the voltage source to appropriate levels for Schmitt Trigger

Voltage source with one AC Signal and one triangular wave signal

D

B

C