ENGR4300

Fall 2005

Test 2A

Name____solution_____________

Section________________________

Question 1 (25 points)___________

Question 2 (25 points) ___________

Question 3 (25 points)___________

Question 4 (25 points)___________

Total (100 points): ______________

Please do not write on the crib sheets.

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS.  No credit will be given for numbers that appear without justification.

Question 1 – Damped Sinusoids and Strain Gauge Bridge (25 points)

You are given a cantilever beam similar to the one you used in experiment 4.  You place two weights on the end of the beam (0.1 kg and 0.5 kg) and you get the following two plots.

Plot 1

Plot 2

1) What is the frequency of plot 1? (Use at least 2 significant figures) (2 points)

f1 = 8 cycles/1.96s = 4.08 Hz

2) What is the frequency of plot 2? (Use at least 2 significant figures) (2 points)

f2 = 17 cycles/1.97s = 8.63 Hz

3) What is the damping constant for plot 1? (Use at least 2 significant figures) (6 points)

(t0,v0) = (0.07,2.3)  (t1,v1)=(1.78,1.0)

1.0 = 2.3 e -((1.78-0.07)	0.83=((1.71)  (=0.5/s

4) Given the following formula, , and assuming that the two data points that you found are ideal, find values for k and m. (6 points)

k = (m+0.1)(2((8.63))^^2	k=(m+0.5)(2((4.08))^^2

k = (2940)m + (294)	k = (657.2)m + 328.6

(2940)m + (294.0) = (657.2)m + 328.6

m = 0.015 kg

k = (0.015+0.1)(2940)=338 kg/s^^2

5) What is the mass of the beam? (3 points)

(0.015) = 0.23 (mb)

mb = .065 kg = 65 grams

6) Using the chart for Young’s Modulus, determine the probable material that the beam is made out of given that the dimensions of the beam are: width = 1.5 cm, length = 20 cm, and thickness = 2 mm. (6 points)

k=Ewt3/4l3

338 = E (0.015)(.002^3)/4(0.2)^3

E=9.0 x 1010 N/m^2

The beam is brass.

For Test B:

The method is the same.

1) f1=3.0 Hz

2) f2=6.48 Hz

3) ( = 0.8/s

4) k=181 kg/s^2  m=0.0092 kg

5) mb = 40 grams

6) E = 6.96 x 1010 N/m^2  The beam is aluminum.

For Test C:

The method is the same.

1) f1=10.3 Hz

2) f2=4.85 Hz

3) ( = 0.6/s

4) k=477 kg/s^2  m=0.0138 kg

5) mb = 60 grams

6) E = 11.6 x 1010 N/m^2  The beam is copper.

Question 2 – Thevenin Equivalent Sources (25 points)

You are told to wire the following circuit in PSpice.  All of the parts in this question refer to this circuit.

Part A:  Finding the Thevenin Equivalent Source with respect to the load resistor, RL, between points A and B.

1) Determine the Thevenin Equivalent Voltage, Vth, with respect to RL. (6 points)

First I must remove RL.  Then I realize that R4 has no current, so the voltage between R2 and R3 is the same as B.  Therefore, I can use a voltage divider to find VR2 and that is the voltage between A and B.

VR2 = 5V[200/(50+200+500)] = 1.33 V

Vth = 1.33V

2) Determine the Thevenin Equivalent resistance, Rth, with respect to RL. (6 points)

When I short out the voltage source, R1 and R3 end up in series.  When I combine them, I get R13 = 50+500 = 550.  This resistor ends up in parallel with R2.  R123 = (550)(200)/(550+200)=146.7.  This resistor is in series with R4.  Therefore, the total resistance between A and B is 146.7 + 400 = 546.7 ohms.

Rth = 546.7 ohms

3) If RL is 2K, what is the voltage between A and B? (3 points)

VL = Vth[RL/(RL+Rth)] = 1.33[2000/(2000+546.7)] = 1.04 V

4) What is the current through the 2K resistor, RL? (2 points)

VL = I (RL)   I = 0.52mA

Part B:  Wiring the circuit in PSpice

1) Of the icons shown at left, which would you use to add the DC source to the circuit?  (2 points)

A

3) Of the icons shown at left, which would you use to add the ground to the circuit? (2 points)

H

2) Of the icons shown at left, which would you use to add a wire to the circuit? (2 points)

B

4) Which PSpice library contains the model for the resistors shown in the circuit above (circle one)? (2 points)

SOURCE	EVAL		ANALOG		BREAKOUT

Question 3 – Op Amp Applications (25 points)

The following questions refer to the circuit on the previous page.

1) What type of op-amp circuit is between points A and B? (1 point)

Inverting Amplifier

2) What type of op-amp circuit is between points C and D? (1 point)

Non-inverting amplifier

3) What type of op-amp circuit is between (B and D) and E? (1 point)

(Weighted) Adder

4) Write an expression for the voltage at point B, VB, in terms of the voltage at A, VA.  Please substitute values. (3 points)

VB = -(Rf/Rin)VA = -(3k/1k) VA      VB = -3 VA

5) Write an expression for the voltage at point D, VD, in terms of the voltage at C, VC.  Please substitute values. (3 points)

VD = (1+Rf/Rin)VC = (1+2k/1k) VC      VD = 3 VC

6) Write an expression for the voltage at point E, VE, in terms of the voltage at B, VB, and the voltage at D, VD.   Please substitute values. (3 points)

VE = -Rf(V1/R1+V2/R2)  VE =-2k(VB/2k + VD/1k)      VE = -VB - 2VD

7) Write an expression for the output voltage at E, VE, in terms of the two input voltages in the circuit, VA and VC. (3 points)

VE = -VB + 2VD	VE = -(-3VA) - 2(3VC)		VE = 3VA - 6VC

8) Identify the signals at points A, B, C, D and E in the PSpice plot below. (10 points)

B and C the same.

Question 4 – Op Amp Analysis (25 points)

Part A:  Below are three op amp circuits you have wired in PSpice.  One will function.  The other two will not.

1)  Which two of the three circuits will not function?  For each circuit explain why you know it will not function. (2 points each = 4 points)

1]   circuit B – positive voltage at negative power terminal (pin 4)

2]  circuit C – positive feedback is unstable

2) Which of the circuits does function?  What type of amplifier is it? (2 points)

circuit A is an inverting amplifier

3) Draw two cycles of the input and corresponding output waveforms for the functioning circuit you identified in part 2.  Specifically identify the amplitude for Vin and Vout.  Label the time scale of the plot. (3 points) (gain = -10)

Part B   In the circuit below, R1 = 2K ohms, R2 = 47K ohms, C2=0.01(F, R4=1k ohms

1) Find the transfer function of this circuit in the form: .  Please substitute values. (3 points)

2) Find an expression (in terms of () for the phase of this circuit for any frequency.  The phase is given by: .   (2 points)

Note that ( is the phase of a negative real number.

3) What is the corner frequency of this circuit in Hz? (2 points)

fc = 1/(2( Rf Cf) = 1/(2()(47k)(0.01u) = 339 Hz

4) For each of the following input frequencies, calculate the phase shift of the circuit AND use the phase to justify whether the circuit is behaving approximately as an inverting op-amp, an ideal integrator, or neither.  (3 points each = 9 points)

5 Hz:

This is about pi.  An inverting amplifier should invert (180 degree phase shift).  	At 5Hz, this circuit acts like an inverting amplifier.

345 Hz:

This is neither pi nor pi/2.  An inverting amplifier should invert (180 degree phase shift) and an integrator should integrate and invert (90 degree phase shift).  This is neither.   At 345Hz, this circuit acts like neither.

34500 Hz:

This is pi/2.  An integrator should integrate and invert (90 degree phase shift).  This is an integrator.   At 34500Hz, this circuit acts like an ideal integrator.

# Text boxes

Circuit A

Circuit B

Circuit C