1) Damped Sinusoids (17 points)

You wire the circuit above in PSpice. You run a simulation and get the following output:

a) Using the output pictured, determine the damping constant, (, of the circuit. (3 points)

b)  What is the resonant frequency of the circuit in Hertz? (3 points)

c) Write an expression in the form  for the output signal. (3 points)

d) The differential equation that governs the behavior of a damped sinusoid is given by  .  In a simple RLC circuit like the one in this question, the angular resonant frequency of the circuit, (0, is given by  and the decay constant, (, is given by .   In the circuit in this question, the value of the resistor, R1, is 40 ohms.  What are the values of the capacitor, C1, and the inductor, L1? (6 points)

e)  You want the resonant frequency of the circuit to be ten times what it is now.  What value of L1 would make this occur? (2 points)

2) Thevenin Equivalent Sources (18 points)

You build the circuit pictured below

Given:  R1=30 ohms, R2=2K ohms, R3 = 3K ohms and R4=2K ohms.

Given: V2=6V

a) Find the Thevenin Equivalent voltage, Vth, of this circuit between point A and point B. (6 points)

b) Find the Thevenin Equivalent Resistance, Rth, of this circuit between point A and point B. (6 points)

c) Redraw the Thevenin equivalent model of the circuit (2 points).

d)  If you place a 5K ohm load on the circuit, what will the output voltage be between A and B? (2 points)

e) What is the current through the 5K ohm load resistor from d? (2 points)

3) Op Amp Applications – Digital to Analog Conversion (25 points)

One family of digital logic we’ll learn about later in the course uses signals that switch discretely between zero and +5V, corresponding to logic levels of 0 (low) and 1 (high), respectively. Here is a chart of the binary numbers from 1 to 16, their decimal equivalents, and corresponding voltage inputs:

c

The following op amp circuit is configured as a digital to analog (D/A) converter. Our D/A converter shown here is a four bit converter: logic voltages at VA, VB, VC, and VD generate an output voltage at Vout.  VD is the lowest order bit corresponding to Vd (in the chart), VC corresponds to Vc, VB corresponds to Vb, and VA corresponds to Va.

Component values for the circuit shown are as follows: R5 = 5k, R6 = 2k, R7 = 10k.

a) The D/A should generate output voltages between 0V for a binary input of 0000 to the full scale value of 15 when a binary input of 1111 is present with a proportional increase in voltage as the binary value increases from 0000 to 1111.  Determine the resistor values R1, R2, R3, and R4 that achieve this in the circuit. (12 points)

# R1 = 			R2 =			R3 = 			R4 =

b) Show the output voltage at Vout will give the correct decimal value for the following two binary input combinations: (6 points).

0100

0110

c)  What would the voltage be at point X, when the input to the circuit is the binary number 1000 (VA=5V)? (2 points)

d) If we increase R5 to 20K and leave all the other resistors the same, what would be the voltage at point X when the input to the circuit is the binary number 1000 (VA=5V)? (2 points)

e) When R5 is 20K and the voltage at X is the one you found in part d), what is the output at Vout?  Why?  (3 points)

4) Op Amp Analysis (19 points)

R1 = R2 = 6K,  R3 = R4 = 8K

a) What op-amp circuit given on your crib sheet does this circuit most closely represent?   (Hint: disregard specific resistor values) (2 points)

b) What are the golden rules of op amp analysis? (2 points)

c) Derive an expression for Vout using the rules for op-amp analysis.  Your result should be in terms of Vin and resistor values R1, R2, R3, and R4 (Do not substitute actual resistor values.)  (You cannot assume R1=R2 or R3=R4).  (12 points)

d) Substitute resistor values in this equation and write the equation for Vout in terms of Vin. (3 points)

Question 5 – Op-Amp Circuit (21 points)

In the circuit below, R1 = 50 ohms, C1 = 0.68(F,  R3 = 3K, and  R4=1K

a) What function is this circuit designed to perform? (2 points)

b) Write the transfer function Vout/V1 for this circuit. (Substitute in the values provided for the components.) (4 points)

c) Over about what frequency range (in Hertz) is the desired function of the circuit reliably performed?  [You can assume that the operation is being performed even when the output amplitude is very small.]  (3 points)

d) Assuming that you have created this circuit in PSpice, how would you set up a simulation to observe how it behaves over a range of frequencies? (3 points)

e) Make a sketch of the frequency response of this circuit.  Mark the corner frequency and the range of frequencies over which the circuit is performing the desired operation (4 points).

f) What type of filter does this frequency response most closely represent? (a low pass filter, a high pass filter, a band pass filter, a band reject filter)? (2 points)

g) During the time that the input to this circuit has a constant slope of 1 V/s, what will be the value of the output voltage? [Assume the circuit is in its operating frequency range.]  (3 points)