ENGR-4300

Fall 2007

Test 4

Name ________________________

Section     1(MR)     2(TF)

(circle one)

Question I (22 points) ___________

Question II (18 points) ___________

Question III (20 points) ___________

Question IV (22 points) ___________

Question V (18 points) ___________

Total (100 points): ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

Question I – Diode Rectifier Circuits (22 points)

The diagram above shows the application of a diode for performing rectification of the signal from the output of the transformer. The sinusoidal source of voltage (V2) has VAMP = 10V and FREQ = 100Hz. Assume that the idealized diode has 0.7V across it during turn-on.

1. (4pt) Sketch V3, given V2, in the figure below:

2. (1pt) If V1 has an amplitude of 120V, is the transformer a step-up or a step-down transformer?

Question I – Diode Rectifier Circuits (continued)

3. (2pt) Now a full wave diode bridge replaces the single diode. Which terminal of Rload, 1 or 2, will have the positive (high) voltage?

4. (4pt) These diodes have the same 0.7V across them when conducting. Given V2 is a 10V sine wave with a frequency of 100Hz, plot the differential voltage across Rload on the axes below.

5. (3pt) What is the peak voltage across Rload?

Question I – Diode Rectifier Circuits (continued)

6. (2pt) If Rload = 2k, what is the maximum (peak) current through it?

7. (3pt) Given V2 above, what must the amplitude of V1 be to provide this output from the transformer?

8. (3pt) Add a 500(F capacitor to the circuit in 3. (redrawn below) between appropriate nodes to reduce the ripple (voltage variations) on Rload.

Question II – Zener Diode Circuits (18 points)

Characteristic curve: The following plot shows the characteristic curve for a Zener diode.

1. (3pt) Mark the following regions on the plot by indicating the boundaries on the x-axis:

Forward bias region			Reverse bias region			Zener region

2. (6) Find the following values and indicate where they are on the plot:

a) Zener Voltage

b) Knee current (current at the point where the voltage across the diode is within 0.1V of the Zener voltage)

c) Turn on voltage

Question II – Zener Diode Circuits (continued)

3. (6pt) Using the Zener voltage found above, what region will each Zener diode be in, Forward Bias (FB), Reverse Bias (RB), or Zener (Z), when the voltage at V1 is each of the following?

| V1 voltage | D1 Region | D2 Region |
| --- | --- | --- |
| -7.5 V |  |  |
| -3.5 V |  |  |
| -1.0 V |  |  |
| 1.5 V |  |  |
| 3.5 V |  |  |
| 7.5 V |  |  |

4. (3pt) What will the current through the circuit be when the voltage at the input is the following?

a) -7.5V:

b) 1.0V:

c) 3.5V:

Question III – LEDs and Phototransistor Circuits (20 points)

A high brightness LED is to be driven by a standard DC source. The source we have available is a 12 Volt wall wart capable of producing up to 6 Watts. We wish to drive this LED in what is called the torch mode, with the high light output required to use it in a flashlight. For this kind of operation, we need a forward bias voltage of 5V and a current of 100mA.

1. (4pt) What is the maximum current that this power supply can produce at its rated voltage? We will need this information for part of this problem.

2. (6pt) Using the 12V power supply, determine the resistance R1 necessary to achieve the desired operating conditions for the diode. Also, determine the power dissipated in the diode D1 and the resistor R1.

Question III – LEDs and Phototransistor Circuits (continued)

3. (8pt) Now, we wish to use this supply to power as many of these diodes as possible. We can either connect them all in series or all in parallel. Shown below are the two options for two diodes.  Find the configurations that support the largest number of diodes in both parallel and series. That is, determine R2 or R3 for the two cases and the power dissipated in both the diodes and the resistors.

4. (2pt) Which configuration allows for the maximum number of diodes to be powered by this source?

Question IV - Diode Limiter Circuits (22 points)

You are given the following circuit:

1. (4pt) What are the minimum and maximum voltages that can ever occur at Vout?

2. (5pt) Sketch Vin and Vout when V1 has: VAMPL = 5V, VOFF = 0V, FREQ = 1kHz.

Question IV - Diode Limiter Circuits (continued)

3. (5pt) Sketch Vin and Vout when V1 has: VAMPL = 5V, VOFF = 2V, FREQ = 500Hz.

4. (5pt) Sketch Vin and Vout when V1 has: VAMPL = 5V, VOFF = -2V, FREQ = 2kHz.

5. (3pt) What is the maximum current that will flow through resistor, R1 = 2K, when V1 has: VAMPL = 5V, VOFF = -2V, FREQ = 2kHz (part 4.)?

Question V – Signal Modulation and Filtering (18 points)

1. (3pt) If the input to a block is the heavy dashed signal in the plot below and the output is the solid signal, what type of modulation is most likely being used?

a) Amplitude Modulation    b) Frequency Modulation    c) Pulse Position Modulation    
d) Pulse Width Modulation.    e) None of the above

2. (3pt) If the top plot below represents the input to a circuit and the bottom the output, in addition to a possible gain stage, what type of operation does the circuit perform?

a) High Pass Filter   b) Low Pass Filter   c) Integration   d) Differentiation   e) Modulation

Question V – Signal Modulation and Filtering (continued)

3. (3pt) What is the main purpose of the capacitor in the audio amplifier circuit below?

a) Boost the gain of the op-amp      b) Match the impedance of the speaker to the op-amp

c) Block low frequencies in the signal     d) Reduce the resistance of the speaker

e) Allow the op-amp to act as a low pass filter

4. (6pt) It is decided to use the circuit below as part of the audio receiver system to pass only frequencies above 50Hz and block frequencies below 50Hz. You are to pick one capacitor and one resistor to be inserted in Z1 and Z2. There are 3 values of resistors: 5k, 50k, & 100k, and 3 values of capacitors: 64nF, 0.4(F, & 7.6(F. Find the best combination of components and show where they will be inserted in the circuit. (Op-amp power supplies are correctly wired.)

5. (3pt) TRUE or FALSE: Swapping the resistor and capacitor around in the circuit in 4. will transform the HPF into a LPF.