ENGR-4300

Spring 2007

Test 3B

Name __________________________

Section _____

Question I (20 points) ___________

Question II (20 points) ___________

Question III (20 points) ___________

Question IV (20 points) ___________

Question V (20 points) ___________

Total (100 points): ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

Question I – Astable Multivibrator (20 points)

The 555 timer circuit shown is found to have an output frequency of 25Hz and a duty cycle of 80% (4/5).

1. (6pt) For C1 = 0.1uF, find R1 and R2.

2. (5pt) Sketch the voltage waveform on pin 2 (which is tied to pin 6). Note the scales on the x and y axes. Start the plot at the time when C1 is charged to its maximum voltage.

3. (4pt) If the value of C1 is halved and Vcc doubled, what are the new frequency and duty cycle of the output waveform on pin 3?

Frequency = _________________		Duty cycle = _______________

Question I – Astable Multivibrator (continued)

4. (4pt) Given a C1 and available resistor values of 1k, 10k, 100k, and 500k, what values of R1 and R2 will produce the highest duty cycle?

5. (1pt) What is the duty cycle in 4.?

Question II – Combinational Logic Circuits (20 points)

1. (6pt) Fill in columns D – G in the table below for the circuit above.

| A B C | D | E | F | G | H |
| --- | --- | --- | --- | --- | --- |
| 0 0 0 |  |  |  |  |  |
| 0 0 1 |  |  |  |  |  |
| 0 1 0 |  |  |  |  |  |
| 0 1 1 |  |  |  |  |  |
| 1 0 0 |  |  |  |  |  |
| 1 0 1 |  |  |  |  |  |
| 1 1 0 |  |  |  |  |  |
| 1 1 1 |  |  |  |  |  |

2. (4pt) Evaluate the expression  and fill in column H in the table above.

3. (5pt) Find the Boolean expression for G the circuit in 1 in terms of A, B, & C (not necessary to simplify).

4. (3pt) Draw the logic circuit for the expression in 2.

5. (2pt) TRUE or FALSE: (circle one) The circuit in 1. is functionally equivalent to that in 4.

Question III – Sequential Logic Circuits (20 points)

In the circuit below, DSTM3 provides an initial reset pulse to the flip flops (top trace). The counter and flip flops all trigger on the falling edge of the clock (2nd trace).

1. (2pt each) Fill in the timing diagram with the signals indicated.

2. (2pt) How would the Q outputs in 1. change if the reset pulse remained low for the duration (10us)?

Question III – Sequential Logic Circuits (continued)

3. (4pt) A 1Hz clock is fed into pin A of a 4-bit counter whose initial state is unknown. After 5s a 1ms clear pulse is applied. What is the state (QD QC QB QA) of the counter after 10 seconds?

a) 0000	b) 1010	c) 0101	d) 1111	e) Can’t be determined

4. (6pt) Determine if the following circuit may be used as a flip flop. Analyze it by filling in the table. Assuming that X and Y will be logical complements, for which AB input combination(s) does the circuit not work properly?

Question IV – Switching Circuits (20 points)

1. (6pt) For the switching transistor circuit above, fill in the voltages in the table.

| A | B | C |
| --- | --- | --- |
| 0V | V | V |
| 0.5V | V | V |
| 1V | V | V |

2. (2pt) For which value(s) of voltage at A in the table will the current through R4 be minimized?

3. (2pt) What is the maximum current that will flow through R1 when A = 1V?

Question IV – Switching Circuits (continued)

4. (7pt) For the relay circuit below, the periodic pulse has an amplitude of 5V, a rise & fall time of 1ms, and the coil has a resistance of 30(. Identify the waveforms of points A, B, C, D & E in the plots. NOTE: one of the waveforms is missing from the plots. You are to add it into the top plot and label it.

5. (3pt) If the relay coil requires a minimum of 100mA for activation, what is the largest value R2 can have?

Question V – Comparators and Schmitt Triggers (20 points)

1. (9pt) For the following input-output curves, circle all that exhibit hysteresis and cross out the functions that can’t be implemented with a single op-amp circuit. (Some may be both.)

2. (2pt) TRUE or FALSE: (circle one) Schmitt Triggers that include an offset reference voltage can have a high threshold voltage > 0V while the low threshold voltage < 0V.

Question V – Comparators and Schmitt Triggers (continued)

3. (6pt) Given the circuit below, find the input voltage switch points for the Schmitt Trigger and the width of the hysteresis band (include units). Note that the supply voltages in the circuit are flipped when compared to the crib sheet drawing.

v+ high = __________		v+ low = __________		Hysteresis Band = ________

4. (3pt) If the input triangle wave to the circuit in 3. has an amplitude of 5Vp-p, what offset must be added to it to obtain a square wave on pin 6 with a 50% duty cycle that switches between 
-10V and +2V?

# Text boxes

6Vdc

C4

| X init | A | B | X final | Y final |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 |  |  |
| 0 | 0 | 1 |  |  |
| 0 | 1 | 0 |  |  |
| 0 | 1 | 1 |  |  |
| 1 | 0 | 0 |  |  |
| 1 | 0 | 1 |  |  |
| 1 | 1 | 0 |  |  |
| 1 | 1 | 1 |  |  |

Vcc

Vin

0

0

0.01uF

R2

R1

C1

X3

555D

1

2

3

4

5

6

7

8

GND

TRIGGER

OUTPUT

RESET

CONTROL

THRESHOLD

DISCHARGE

VCC

Rload

0

R1

1k

V2

9v

Q1

Q2N2222

R4

1k

R5

1k

U2

Relay_SPDT_nb

COM

A

B

NC

NO

R2

30

Vpulse

A

B

C

D

QA

QB

QC

QD

E

Time

0s

5ms

10ms

15ms

20ms

25ms

30ms

0V

5V

10V

0V

10V

V1

1Vac

0Vdc

R1

1k

R2

1k

Q1

Q1

9Vdc

0

Q2

Q2

R3

1k

1

2

R4

1k

7408

U1A

A

B

C

3

U1B

7408

4

5

6

U1C

7408

9

10

8

U2A

7404

1

2

U2B

7404

3

4

U3A

7427

1

2

13

12

2

-

+

3

A

B

C

D

F

G

E

V+

7

V-

4

OUT

6

OS1

1

OS2

5

0

Vtriangle

+2V

-10V

R1

3k

R2

1k

+2V