# ENGR-4300

# Fall 2008

# Test 2

# Name: _______SOLUTION__________

# Section:	1(MR 8:00)	2(TF 2:00)

# (circle one)

# Question I (20 points): ___________

# Question II (20 points): ___________

# Question III (20 points): ___________

# Question IV (20 points): ___________

# Question V (20 points): ___________

# Total (100 points): ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

# Question I – Bridges and Damped Sinusoids (20 points)

You are given a cantilever beam similar to the one you used in experiment 4.  You place two weights on the end of the beam one at a time (0.1 kg and 0.7 kg) and you get the following two plots (may not be in order of mass listed).

# 1) (2pt) What is the frequency of plot 1?  (Use at least 2 significant figures)

# Question I – Bridges and Damped Sinusoids (continued)

# 2) (2pt) What is the frequency of plot 2?  (Use at least 3 significant figures)

# 3) (6pt) What is the damping constant for plot 1, mark the points on the plot?  (Use at least 3 significant figures)

# 4) (6pt) Given the following formula, , and assuming that the two data points that you found are ideal, find values for k and m.

# Question I – Bridges and Damped Sinusoids (continued)

# 5) (2pt) What is the mass of the beam?

# 6) (2pt) Using the chart for Young's Modulus, determine the probable material that the beam is made out of given that the dimensions of the beam are:  width = 1.5 cm, length=15 cm, and thickness = 2 mm.

# Question II – Thevenin Equivalents (20 points)

# 1) (7pt) Find the Thevenin equivalent voltage with respect to A and B for the circuit shown above)  Hint: Vth=VA-VB so find VA then VB

Note: forgot to put R5 at probe B negate R5

# Question II – Thevenin Equivalents (continued)

# 2) (6pt) Find the Thevenin equivalent resistance with respect to A and B for the circuit shown above.

# 3) (5pt) Draw the Thevenin equivalent circuit with a load resistor RL of 3K between points A and B

# 4) (2pt) What is the voltage across RL?  Hint: Also the voltage at point VA

# Question III – Op-Amp Applications (20 points)

Assume the following components in the above circuit:

# 1) (1pt) The circuit above is an amplifier you've seen.  What type of amplifier is it?

# 2) (3pt) Write an equation for the output C (Vc) in terms of the input voltages V2 and V3.  Simplify (Do not have to enter voltage values)

# Question III – Op-Amp Applications (continued)

# 3) (16pt) Sketch and label one cycle of the input at V2 (point B), the input at V3 (point A) and the output at C (Vc) on the plot below

(extra credit +2 if plotted second graph with (15V supplies clipping output)

# Question IV – Op-Amp Analysis (20 points)

# 1) (2pt) What op-amp circuit given on your crib sheet does this circuit most closely represent?

a. Inverting Amplifier   b. Non-inverting Amplifier   c. Adder   d. Differential Amplifier

e. Practical Active Differentiator

Non-inverting Amplifier

# 2) (2pt) Redraw the circuit combining and resistors that are in parallel or series and find the combined values.

15k =10k + 5k     3k = (4k x 12k)/(4k + 12k)

# 3) (2pt) What are the two golden rules of op-amp analysis?

# 1. The output attempts to do whatever is necessary to make the voltage difference between the

inputs zero (the + and – terminals will have the same voltage).

# 2. The inputs (+ and – terminals) draw no current.

# Question IV – Op-Amp Analysis (continued)

# 4) (2pt) Using a different circuit below, if Vin = 1V on the ‘+’ input of the op-amp, what is the voltage on the ‘–‘ input?

V-= V+ = Vin = 1V   (Golden Rule)

# 5) (3pt) From 4), how much current is flowing through the 2k resistor to ground?

# I2k = V-/R = 1V/2k = 0.5mA

# 6) (3pt) By the Golden Rules, how much current in 4) is flowing through the 10k resistor from Vout to V- (the connection point between the 2 resistors)?

# By the Golden Rule, all the current in the 2k must come from the 10k; I10k = I2k = 0.5mA

# 7) (3pt) What is Vout for Vin = 1V?

# 8) (2pt) What is the gain of this op-amp circuit?

# 9) (1pt) For an ideal op-amp in 4), what is the maximum value the input voltage Vin can have before the output will not be able to exhibit the full amplification from 8)?

Max output = 9V ((9V batteries)        Vin = 9/Gain = 9/6 = 3/2V = 1.5V

# Question V – Op-Amp Integrators and Differentiators (20 points)

# 1) (2pt) What function is this circuit designed to perform?

# Practical Miller Integration

# 2) (4pt) Write the transfer function Vout/V1 for this circuit. (Substitute in the values provided for the components.)

# 3) (3pt) For which frequencies will the circuit perform the desired function?

a. Low frequencies below (c		b. Only a mid band of frequencies around (c

c. High frequencies above (c

c. High frequencies above (c

# 4) (3pt) Find the corner frequency for the circuit in Hz.

fc = 1/(2(RfCf) = 1/(2( x 5k x 1() = 31.83Hz

# Question V – Op-Amp Integrators and Differentiators (continued)

# 5) (2pt) Redraw the circuit with an appropriate substitution for the capacitor as f ( 0 for when the input V1 has a very low frequency.

Replace C with open circuit

# 6) (4pt) Show that simplification of the transfer function from 2) for small ( gives the same results as the analysis of the redrawn circuit in 5).

# From 2):

# From the inverting op-amp in 5): AV = -Rf/Ri = -5k/1k = -5

# 7) (2pt) Sketch the output of the original circuit in 1) to a square wave input on the axis below. Show the correct shape of the waveform but don’t worry about the amplitude scaling.