ENGR-4300

Fall 2008

Test 1

Name ________________________

Section ____

Question I (20 points) ___________

Question II (20 points) ___________

Question III (20 points) ___________

Question IV (20 points) ___________

Question V (20 points) ___________

Total (100 points) ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

Question I. Resistive circuits (20 points)

Given: V1=5 volts.  R1= 2000, R2= 1000, R3= 500, R4= 400

1) (7 pts) Find the total resistance of the circuit.

2) (5 pts) Find the voltage across R1. (Note that this is not referenced to ground.)

3) (6 pts) Find the current through R4.

4) (2 pts) Which resistor has the largest voltage drop across it?

Question II – Filters (20 points)

You are given the following circuit. The input at V1 is a 20V AC signal. Leave all answers for 1) – 4) in terms of R1, R2, R3, C1, C2, L1, and L2. V0 and V2 are measured with respect to ground.

1) Redraw the circuit for ( ( 0 with appropriate simplifications for the impedances and find V0 and V2. (5 pts)

2) Redraw the circuit for ( ( ( (high frequencies) with appropriate simplifications for the impedances and find V0 and V2. (5 pts)

3) At what value of ( (greater than 0 and less than () would you expect to find V0 minimized? (3 pts)

4) At what value of ( (greater than 0 and less than () would you expect to find V0 maximized? (3 pts)

5) What special name is given to the ( values in 3) and 4)? (2 pts)

6) TRUE or FALSE: If V1 had a DC offset and ( is neither the value in 3) nor 4), the output V0 would also have a DC offset. (2 pts)

Question III – Transfer Functions (20 points)

1) For ( = 10, a circuit has a transfer function . Find the magnitude and phase of H(j10). (4 pts)

2) For an H(j5) = 0.75/(/3 and Vin(t) = 2cos(5t - (/2), find Vout(t). (6 pts)

The plot below shows the input (solid thin line) and output (dashed wide line) of a circuit whose transform is H(j() = Vout(j()/Vin(j(). Note that the time axis is from 100ms to 250ms.

3) Determine ( (radians/s) for the input and output signals? (2 pts)

4) Determine the magnitude of H(j( at this frequency. (3 pts)

5) Determine the phase of H(j) at this frequency? (3 pts)

6) If H(j() is a 1st order LPF, ( is most likely: (2 pts)

a. the resonant frequency     b. in the pass band    c. in the stop band    d. the corner frequency

Question IV – Signals, Transformers and Inductors (20 points)

1) Given the circuit above, for what value of RL will the power in RL be maximized? (2 pts)

2) What is the power dissipated in RI and in RL? (4 pts)

3) What is the efficiency of the circuit in terms of the power dissipated in RL over the total power dissipated in the circuit ? (2 pts)

4) Now with RI = 1k( and RL = 100(, assume PRL = 1.0W and PRI = 10.0W. What is the efficiency of this circuit  (2 pts)

5) An ideal transformer is added to improve the efficiency as shown above. The desire is to have Zin of the transformer at the dashed line equal to RI (1k(). What turns ratio ‘a’ will do this? (5 pts)

6) TRUE or FALSE: the expected efficiency of the modified circuit in 5) is 50%. (1 pt)

7) For the transformer with turns ratio a = 5, if L1 = 10mH what is L2? (4 pts)

Question V – Instrumentation, PSpice and components (20 points)

In experiment 1, you wired a circuit similar to the one below using real components and in PSpice:

1) (6 pts) What does this circuit do? What do R1, R2, and R3 represent?

2) (3 pts) Suppose V1 has a frequency of 0.5kHz, an amplitude of 400mV, and a DC offset of 0.  You want to run a transient analysis.  How would you set up the simulation screen below to show exactly 3 smooth cycles of the output wave? (Fill in the three empty boxes.)

3) (3 pts) If you set up this transient simulation, what would be the frequency (in Hz) and the approximate amplitude (in mV) of the signal at the point of the voltage probe?

4) (5 pts) If you replaced R2 with a resistor with color code orange-black-red-gold, what would be the frequency (in Hz) and the approximate amplitude (in mV) of the signal at the point of the voltage probe?

5) (3 pts) To get an IOBoard function generator to output the signal in the circuit above, the voltage must be specified as:   a. 0.4V       b. 0.2Vp-p     c. 0.8V      d. 0.8Vp-p      e. none of these