ENGR-4300

Spring 2008

Test 2 CONFLICT

Name: _________________________

Section:	1(MR 8:00)	2(TF 2:00)	3(MR 6:00)

(circle one)

Question I (23 points): ___________

Question II (16 points): ___________

Question III (16 points): ___________

Question IV (20 points): ___________

Question V (25 points): ___________

Total (100 points): ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

Question I – Bridges and Damped Sinusoids (23 points)

You wire the circuit above in PSpice. You run a simulation and get the following output:

1) (3pt) Using the output pictured, determine the damping constant, (, of the circuit.

2) (3pt) What is the resonant frequency of the circuit in Hertz?

3) (3pt) Write an expression in the form  for the output signal.

Question I – Bridges and Damped Sinusoids (continued)

4) (6pt) The differential equation that governs the behavior of a damped sinusoid is given by .  In a simple RLC circuit like the one in this question, the angular resonant frequency of the circuit, (0, is given by  and the decay constant, (, is given by . In the circuit in this question, the value of the resistor, L1, is 40mH. What are the values of the capacitor, C1, and the inductor, R1?

5) (2pt) What new value of capacitance for C1 would make the resonant frequency of the circuit be ten times higher than what it is now?

Question I – Bridges and Damped Sinusoids (continued)

6) (6pt) Below are 2 variations of bridges circuits. The left configuration is the one used in Experiment 5. The right configuration has both strain gauges on the top of the beam. They are configured with a DC voltage source as shown below. Note that the nominal resistance of each strain gauge is represented as R and the change in the resistance of the strain gauge due to the deflection of the beam is dR. The voltage source is set to 10V. The output voltage observed is A – B. Using this information, determine the sensitivity to deflection in terms of R and dR of each circuit and which is more sensitive.

Question II – Thevenin Equivalents (16 points)

1) (5pt) Find the Thevenin equivalent voltage with respect to A and B for the circuit shown above left with the Thevenin equivalent circuit on the right.

2) (5pt) Find the Thevenin equivalent resistance with respect to A and B for the circuit shown above left.

3) (4pt) If terminal A is shorted to terminal B in the left circuit, what is the maximum current that will flow through the connection? (Hint: use what can be done with Thevenin equivalent circuits to simplify this calculation.)

4) (2pt) How would the Vth and Rth values change if the power supply voltage in the left circuit doubled?

Question III – Op-Amp Applications (16 points)

Assume that (9 Volt power supplies have been properly connected to all three op-amps in the circuit above.

1) (3pt) The circuit has 3 op-amps labeled as U1, U2, and U3. State what the op-amp circuit is for each. Choices are: 1. Follower/Buffer, 2. Inverting Amp, 3. Non-inverting Amp, 4. Differentiator,

5. Integrator, 6. Adding (Mixing) Amp, 7. Difference (Differential) Amp.

U1 Circuit: _______________     U2 Circuit: _______________     U3 Circuit: _______________

2) (6pt) Determine the voltage (a function of t), relative to ground, at points VA and VB as functions of Vin(t) with Rin = 40k, Cf = 25(F, Cin = 33(F, Rf = 10k, R1 = 5k, R2 = 3k, and R3 = 15k.

a) Voltage at point VA(t):

b) Voltage at point VB(t):

Question III – Op-Amp Applications (continued)

3) (3pt) Determine the output voltage, Vout(t), as a function of VA(t) and VB(t).

4) (4pt) Now find Vout(t) as a function of Vin(t).

5) (2pt) What is one practical implementation problem with this circuit that distinguishes it from the ideal circuit?

Question IV – Op-Amp Analysis (20 points)

R1 = R2 = 6k,  R3 = R4 = 8k

1) (2pt) What op-amp circuit given on your crib sheet does this circuit most closely represent? (Hint: disregard specific resistor values)

2) (2pt) What are the two golden rules of op-amp analysis?

Question IV – Op-Amp Analysis (continued)

3) (12pt) Derive an expression for Vout using the rules for op-amp analysis. You must use Ohm’s Law and current laws to describe how the op-amp functions by the golden rules. Your result should be in terms of Vin and resistor values R1, R2, R3, and R4. (Do not substitute actual resistor values. You cannot assume R1=R2 or R3=R4.)

4) (4pt) Substitute resistor values in this equation and write the equation for Vout in terms of Vin.

Question V – Op-Amp Integrators and Differentiators (25 points)

In the circuit below, R1 = 1k(, C1 = 0.68(F, R3 = 3k(, and R2 = 1k(

1) (2pt) What function is this circuit designed to perform?

2) (4pt) Write the transfer function Vout/V1 for this circuit. (Substitute in the values provided for the components.)

3) (4pt) Over about what frequency range (in Hertz) is the desired function of the circuit reliably performed?  [You can assume that the operation is being performed even when the output amplitude is very small.]

Question V – Op-Amp Integrators and Differentiators (continued)

4) (4pt) Assuming that you have created this circuit in PSpice, how would you set up a simulation to observe how it behaves over a range of frequencies?

5) (4pt) Make a sketch of the frequency response of this circuit.  Mark the corner frequency and the range of frequencies over which the circuit is performing the desired operation.

6) (3pt) What type of filter does this frequency response most closely represent?

a) low pass filter    b) high pass filter    c) band pass filter    d) band reject filter

7) (4pt) for an input V1(t) = cos(6000t), what would be the amplitude of the output signal? [Assume the circuit is in its operating frequency and voltage range.]

8) (EXTRA CREDIT 1pt) At low frequency this circuit in 5) acts like a __________________.

Fill in the blank using one of the following: a) Inverting Amplifier, b) Non-inverting Amplifier, 
c) Differential Amplifier, d) Adder, e) Integrator, f) Differentiator, g) none of a thru f.