ENGR-4300

Spring 2008

Test 4

Name ______________________

Section     1(MR 8:00)     2(TF 2:00)     3(MR 6:00)

(circle one)

Question I (24 points) ___________

Question II (16 points) ___________

Question III (15 points) ___________

Question IV (20 points) ___________

Question V (25 points) ___________

Total (100 points): ______________

On all questions: SHOW ALL WORK. BEGIN WITH FORMULAS, THEN SUBSTITUTE VALUES AND UNITS. No credit will be given for numbers that appear without justification.

Question I – Diode Rectifier Circuits (24 points)

The diagram above shows the application of a diode bridge for performing rectification of the voltage from the output of the transformer. The sinusoidal source voltage V1 = 120VRMS and 
R1 = 5kΩ.

1. (4pt) Knowing that the voltage amplitude is  larger than the RMS voltage, what transformer turns ratio n:1 will give as close as possible to a 6V amplitude at V2? (n should be rounded to an integer.)

2. (4pt) What will the actual peak voltage be on the output of the full wave bridge (across R1). Let the idealized diodes have Von = 0.6V and V2 is the voltage from the turns ratio in question 1?

3. (3pt) Given R1 above, what is the peak current that will flow through any of the 4 diodes?

Question I – Diode Rectifier Circuits (continued)

4. (4pt) For a 60Hz input voltage V1 a capacitor is added in parallel with R1 to reduce the ripple in the voltage across the load resistance so that the droop is less than 0.25V. Which of the following values is the minimum capacitance necessary to achieve this?

a) 1(F		b) 17(F	c) 33(F	d) 100(F

5. (3pt) It is decided to use a 680(F capacitor to filter the supply voltage. What 3 digit code will be written on this capacitor to indicate its value?

6. (6pt) For a quick calculation of the voltage droop with the 680(F capacitor and 5kΩ load resistance, assume a 5V amplitude 50Hz sine wave has been ideally full wave rectified 
(Von = 0V). Use the period between adjacent peaks as the maximum droop time and assume the exponential decay can still be modeled as a straight line in this interval. With these simplifications, how much will the voltage droop from its 5V maximum value?

Question II – Zener Diode Circuits (16 points)

Below are 2 Zener diode limiter circuits. Vz = 7V for D1 and Vz = 4V for D2.

1. (6pt) For the left-hand circuit, on the axes below sketch the output voltage at the probe for the 3 inputs below.

Question II – Zener Diode Circuits (continued)

2. (4pt) For the right-hand circuit, on the axes below sketch the output voltage at the probe for the 2 inputs below.

Question II – Zener Diode Circuits (continued)

3. (4pt) Sketch the voltage input-output curve for the left-hand circuit above. Be sure to scale the axes.

4. (2pt) TRUE or FALSE: A full wave bridge rectifier with all the diodes replaced with Zener diodes (Vz = 5V) would still be able to rectify a 5.5V amplitude input sine wave (V2 on the circuit in question I-1) with the same output waveform as with regular diodes (assuming the Von voltages are all 0.7V).

Question III – LEDs and Phototransistor Circuits (15 points)

Above is a typical optical isolation circuit with an LED/phototransistor pair. The logic gate and inputs may be in a cage whose reference voltage is 5kV higher than the phototransistor and relay circuit, but the “optical isolation” removes the danger of high voltage getting through.

1. (6pt) Fill in the following table:

| A | B | Relay (on or off?) | LED C (on or off?) | LED D (on or off?) |
| --- | --- | --- | --- | --- |
| 0 | 0 |  |  |  |
| 0 | 1 |  |  |  |
| 1 | 0 |  |  |  |
| 1 | 1 |  |  |  |

2. (5pt) Assuming the resistance of the relay coil is negligible but 200mA is needed to turn it on, what is the maximum resistance value R can be if the on-resistance of the phototransistor is 15Ω?

3. (4pt) Using the phototransistor on-resistance of 15Ω, setting R = 5Ω and assuming the phototransistor behaves like an ideal switch when it is turned off, what are the minimum and maximum voltages at E, the collector of the transistor?

Question IV - Diode Limiter Circuits (20 points)

1 (6pt) Design a diode limiter circuit in the square, using stacked series standard Silicon diodes, that limits Vout to a maximum of +2.1V and a minimum of -6.3V.

2. (4pt) Sketch Vin and Vout when Vin is a 1kHz triangle wave with an 8V amplitude and a -2V offset.

Question IV - Diode Limiter Circuits (continued)

3. (4pt) If all the diodes in this limiter circuit were replaced with diodes whose forward bias voltages (Von) are 0.6V, what would the maximum and minimum output voltages become?

4. (6pt) Can the circuit below, with appropriate values for Vz, be made to match the requirements in question IV-1? If not, explain why not. If so, what values are needed as Vz for Zener 1 and Zener 2? Von for all diodes is the same as in IV-1 above.

Question V – Signal Modulation and Filtering (25 points)

A modulated signal is to be filtered to remove the effects of the modulation and other noise. The desired signal is from 100Hz – 8kHz. The undesired parts of the signal are below 50Hz and above 10kHz. Design a combination of filter types (low pass and/or high pass) that will remove everything except the desired signal. It has been decided that the filters should be in series (cascaded) as shown below. The Zs in the op-amp circuits represent complex impedances and may be combinations of resistors and capacitors. (Hint: one of these filters was used in Project 4.)

1. (4pt) For each filter determine the appropriate type.

Filter 1: ____________________		Filter 2: _____________________

2. (6pt) For each filter determine the corner frequency.

Filter 1 fc: _________________		Filter 2 fc: _____________________

Question V – Signal Modulation and Filtering (continued)

3. (8pt) Using 20kΩ resistors and whatever capacitor values are necessary, draw the circuits for Filter 1 and Filter 2 with the correct components replacing the Zs above.

4. (4pt) Write down the transfer function, H(j(), for each filter with numerical values for the coefficients.

5. (3pt) Which type of filters, Miller integrators or practical differentiators, have problems due to inherent noise in signals?

# Text boxes

Load Resistor

Transformer

Zener2

V2

Zener1

V3

V1

0

Vout

V

Vout

Vin

+

R1

1k

-

n:1

DIODE BRIDGE

Vin

V

1k