Project 4 Circuits

In project 4, you will build a transmitter and a receiver.  The transmitter uses a 555-timer to modulate a signal.  The output of the transmitter is a string of frequency modulated light pulses.  The receiver uses a phototransistor to take in the light from the pulses.  It then uses an inverting op-amp and an audio amplifier to amplify the signal so that it can be played on a speaker.  The original receiver circuit you will build does a poor job of reconstructing the signal (although it is still audible).  For this project, you will be adding an integrator to the receiver to create a more accurate reconstruction of the original input wave.  We are providing you with a copy of the two initial circuits ahead of time, so you can get started building them if you have completed experiment 8.

Transmitter Circuit

Receiver Circuit

Output after smoothing capacitor

Output before smoothing capacitor

Before integration and smoothing