Project 4: Optical Communications Link

In this project you will build a transmitter and a receiver circuit.  The transmitter circuit uses pulse frequency modulation to create a series of light pulses that encode an audio signal.  The receiver takes in the light pulses, demodulates them, amplifies the signal back to the level the audio amplifier needs to see, and sends it through an audio amplifier to a speaker where it can be heard.  Your initial design will reconstruct the input to create an audible signal of poor quality.  In the final design, you will modify the circuit to create a much better quality demodulated audio signal.

The figure above shows an input signal (top) and its pulse frequency modulated equivalent. Simply averaging this signal will demodulate it to some extent. The initial design for the receiver circuit provides this functionality to a small degree more-or-less by accident.  If you enhance the time-averaging ability of the circuit with the addition of an integrator, you will be able to improve the reconstruction of the audio signal.  The integration, however, will attenuate the signal level somewhat. To make up for this, you will have to adjust the gain of the circuit after the integrator is added.  You will also be asked to add a smoothing capacitor to the circuit to further improve your output signal.  The modified circuit is to be tested to be sure that it is an improvement over the initial design.

Another part of this project is to determine what each block of the circuit you are building does.

The piece of the circuit between each of the marked points performs is a sub-circuit that performs some function.  You have encountered most of these smaller circuits sometime during the semester.  (Information about the audio amplifier is contained in this handout.)  You should be able to identify the function of each block and show that the block is functioning as expected by comparing the signal before the block to the signal after it.

Initial Design

In the initial design of this circuit you will build a transmitter and a receiver.  You will also look at the function of a PSpice model of the circuit.

Transmitter Circuit

The initial transmitter circuit is pictured below.

In this circuit, Vin is your input signal.  In this project, you will use the function generator and an audio source as inputs.  Note the location of the three points: A, B and C.  These points define the input and output to the blocks in the circuit.  For example, the block between A and B is a DC blocking capacitor.  It keeps the DC offset introduced by the 555 timer from interfering with the input signal and vice versa.

Receiver Circuit

The initial receiver circuit is shown below.

In this circuit, your input is the light pulses being detected by the phototransistor.  The output is a demodulated and amplified signal played on a speaker.  Again, note the locations of the points D, E, F, G and H.  You will be measuring the voltage signals at these points and defining the circuit blocks between them.

The audio amplifier

Your circuit contains an audio amplifier.  Details on this block of the circuit are contained in the spec sheet for the 386 amplifier.  The following image is taken from that source.

Note the addition of the capacitor to create a gain 10 times larger.  You may need to add this in your final design, but it is not recommended in the initial design.  Also note the low-pass RC filter has different components in our circuit than in the one shown.  If you use the filter values from the spec sheet, the output of your initial design will not be audible at higher sampling frequencies because the filter will block out the high frequency sample pulses.  If you want, you can use the 0.05u—10 combination in your final design.

PSpice Model

We will give you a PSpice circuit that models the function of the initial transmitter and receiver circuit combination.  You should generate PSpice output showing the function of each circuit block and also the function of the circuit as a whole.

The model: The picture on the next page shows the different pieces of the model.  An audio source is approximated using two sine wave sources.  The transmitter circuit is separated from the receiver circuit with a buffer.  There is also a pot that creates the difference in amplitude between the pulses generated by the transmitter and the pulses picked up by the phototransistor.  The audio amplifier in the receiver is modeled with a different amplifier (E) than the 386 used in the real circuit.  (PSpice does not have a 386).  In order to keep the amplitude of the output at the same order of magnitude as the input, the gain on this amplifier (2) is 1/10 of the gain on the 386 without the optional capacitor.  The picture also shows the locations you will use to add the circuit elements you need for your final design.

Run the simulation:  Start by running the simulation provided.  Voltage markers have been added at each of the eight points (A-H). Remember that the initial design should give you a poor quality reproduction of your input signal.  Therefore, you should expect the model of the initial design to give you a poor quality reconstruction of the signal at the output.  The input (point A) and output (point H) of the simulation should look something like this:

Determine your sampling frequency: The sampling frequency in the PSpice model is  representative of a good sampling frequency for your circuit.  It is hard to determine exactly what this frequency is by looking at the pulses because the frequency of the pulses changes with the input signal.  You can get a reasonable average by calculating the frequency of the 555 timer circuit using the astable mode equations and the values of the components in the R-R-C combination.  Be sure that the PSpice frequency and the actual sampling frequency of your transmitter circuit match reasonably well when you take your data and design your integrator.  You can match the frequencies either by turning the 100K pot in the actual circuit and/or by changing resistor R3 in the PSpice model.

Examine the different blocks:  Once you have the simulation running, try looking at the input and output of each block separately.  (For example, look at the signals at point A and point B only.  Which has the DC offset? Why?)  This will give you an idea of what the block is doing and also what to expect from your circuit.

Building and Testing the Circuits

Build the circuit as shown in the circuit diagram.  Leave out the optional 10(F capacitor.  You may need it after you add the integrator, but it will probably amplify the signal too much in the initial design.  If the amplification is too high, the audio output will sound distorted.  Test your circuit using a signal from the function generator representative of an audio wave.  When the circuit works, have a staff member sign off on it and take your data.

test input signal:  The transmitter is a 555-timer circuit very similar to an astable multivibrator.  The only difference is that instead of generating a regular string of pulses, it generates a string of pulses which vary in frequency in response to the input signal at pin 5.  It is best to use a sine wave to debug this circuit.  A typical audio signal is pictured below.  Note that the signal below has several frequencies.  There are about 10 cycles of a typical wave in a 5 ms division.  This corresponds to a frequency of about 2K hertz.  Also note that the amplitude reaches a maximum of about 400mV.  If we assume that this audio signal is typical of what we will get from our audio source, we should set the function generator to a frequency of 2K and an amplitude of 400mV.

no common ground: The two circuits should NOT have a common ground.  They should be completely separate and the transmission of the light pulses should be the only interaction.

orientation of the phototransistor: The phototransistor works in both orientations. In our experience with this circuit, it is best to use it in the orientation that generates signals of maximum

amplitude.  Since we have different brands of phototransistors in circulation, we cannot tell you directly what orientation this is.  The best thing for you to do is to test your phototransistor in both orientations and choose the one that gives you the strongest transmission signal.

verify that the transmitter is working:  You should make sure that the pulses from your circuit are modulated by observing the voltage at the input (point A) and the voltage at the output (point C).  The output should look like a pulse modulated signal.  (If the input is low, the pulses should get closer together and if the input is high, the pulses should get farther apart.)  As you turn the pot, the frequency of your input signal should change.

Set your sampling frequency:  CD quality sound uses 44.1 samples per second to recreate an audio signal.  Each pulse in your modulated signal is like a digital sample.  A high sampling rate is desirable if you want to get high quality sound from your circuit.  To vary your sampling rate, turn the 100K pot.  To determine your sampling frequency, find the frequency of the pulses using the scope.  You will not be able to get an exact measure of the sampling frequency of your circuit because it changes.  However, you can get an estimate by averaging over several cycles.  Since you will be comparing your data to the PSpice model (and using it to design your integrator), it is important that the sampling frequencies for your actual circuit and your PSpice circuit match fairly well.  Either try to match your circuit to the PSpice or change the sampling rate of the PSpice circuit by altering the value of R3.

getting the receiver to work:  The receiver circuit is more complicated than the transmitter circuit.  If yours does not work, try debugging it in pieces.  Check to see that the phototransistor is generating a set of pulses that corresponds to the pulses from the LED.  Check to see that the inverting amplifier is making the pulses bigger.  Make sure the volume pot alters the amplitude of the signal.  Finally, check to see if the audio amplifier amplifies the signal again.  If you identify a block that does not work, debug it before you continue on to the next one.

your audio signal:  You will need to demonstrate that your circuit works using the function generator and a real audio signal.  The computers in the studio have output jacks in the front.  All the computers also have a copy of Winamp installed.  You can bring your own music or find some on the internet.  If you prefer, you can use your laptop or a portable audio device.  Make sure that you use the scope to check the amplitude of your input signal.  Set the volume of your signal so that it corresponds roughly to the 400mV amplitude of the test input.  If you cannot turn the volume up that high, you may need to use another input device.  Do not let your input amplitude exceed 1V.  This will interfere with the 555 timer’s ability to sample the input effectively.

signature:  When your circuit works, have a staff member listen to the circuit with the sine wave input and with the audio input.

Personal Stereo _____________    Witnessed ________________

Function Generator __________ Witnessed _________________

Taking your data

Take data showing the input and output to each block of the circuit and also the overall function of the circuit.  The effect of the circuit on the simple sine wave from the function generator is much easier to understand.  Therefore, we ask you to take most of your data using this signal.  No signatures are required.

take PSpice data:  Before you take plots of the PSpice simulation, verify that the sampling frequency is about the same as your circuit and that the amplitude of the signal at point D is similar in both the simulation and the actual circuit.  If not, you can alter the sampling frequency by changing R3 and the amplitude at D by changing the set parameter of the pot at point C.  If you want in System (A-H), you can invert the output at H (multiply it by -1) to get a better visual comparison with the input at A.

Block (A-B) : _______	Block(B-C): ______		Block(C-D):_____

Block (D-E) : _______	Block(E-F): ______

Block(F-G):______		Block (G-H) : _____		System(A-H): _____

take function generator data:  The following is a list of the Agilent plots you should generate.  For each block put one signal on channel 1 and the other on channel 2.  Be careful to keep track of which signal is which.  If you want in System(A-H), you can invert the output at H with the scope to get a better visual comparison with the input at A.

Block (A-B) : _______	Block(B-C): ______		Block(C-D):_____

Block (D-E) : _______	Block(E-F): ______

Block(F-G):______		Block (G-H) : _____		System(A-H): _____

take audio data: Take the following additional data using your audio signal as input.  If you want in System(A-H), you can invert the output at H with the scope to get a better visual comparison with the input at A.

Block(E-F): ______	   System(A-H): _____

Comparison

The final step in the initial design is to compare the output of the PSpice model to the output of the actual circuit.  Are they similar?  Also examine the function of each circuit block.  Does each block work as expected?

Final Design

The initial design for the receiver of this project reconstructs the signal well enough to be audible, but it does a very poor job.  You can improve the output of your circuit by adding an integrator and a smoothing capacitor.  Your final signal at (point H) should look and sound much more like the original signal coming from your audio device at (point A).

Adding an integrator

The first change you will make to your circuit is to add an integrator.

What the integrator should do: When you integrate the modulated signal, you take advantage of the fact that the pulses vary in frequency.  Your pulses (at point E) are square waves centered around zero.  When you are on the positive part of the pulse, the signal (the integration of a positive constant) ramps up.  When you are on the negative part of the pulse, the signal (the integration of a negative constant) ramps down.  Since the pulses vary in frequency (and width) with the signal, adding this integration will bring out the variation in the amplitude of the original signal.  The figure below shows the input (point A) and the output (point H) of the PSpice model with an appropriate integrator added.

There are a few things you should note in this output.  The first is that the signal is inverted.  Another is that there is a time shift between the input and the output.  The third is that, although the pulses are still there, the signal itself now looks much more like the original input signal at A.

Types of integrators:  You can either add a passive or an active integrator to your circuit.  Both work well, so it is a matter of preference.  Both are discussed in this section:

- Passive Integration

Below is a picture of a passive (approximate) integrator.  It only works at higher  frequencies. When  >> c=1/RC, then  .  If you add this integrator, you will add it at point E.

When you add this integrator, you will notice a marked decrease in the amplitude of your signal.  You can increase the signal amplitude again by adding the 10(F capacitor to the audio amplifier.  If this is not enough (or too much), you can adjust the gain on the inverting amplifier to get the signal to a level that is comfortable for your speaker.

- Active Integration

Below is a picture of an active integrator. To add this type of integrator, you can modify the inverting amplifier in your circuit by adding a capacitor to the feedback path.  This integrator also does not work well at very low frequencies.

When   >> c = 1/(RfC), then .

When you add this integrator, you will notice a marked decrease in the amplitude of your signal, as well.  You can increase the signal amplitude again by adding the 10(F capacitor to the audio amplifier.  If this is not enough (or too much), you can adjust the gain on the inverting amplifier (by changing Ri) to get the signal to a level that is comfortable for your speaker.

Designing your integrator:  You want your integrator to work on an audio signal.  In the PSpice model, the sample input frequency varies between 500 Hz and 4k Hz.  This range should be adequate.  If you want to, you can look closely at the audio signal you are using and determine its lowest and highest frequencies.  If they fall outside this range, change the frequencies of the two sine wave sources.  You need to choose a frequency for your integrator much lower than 500 Hz that will still integrate 4k Hz AND preserve enough of the amplitude so that you still have a signal.  With either integrator, you need to choose R and C such that your chosen frequency is much less than the frequencies you want to integrate, f << 1/(2(RC).  In the passive integrator, you can choose R arbitrarily, in the active integrator, R is the value of your feedback resistor.

Testing your choice with PSpice: Once you have chosen an integrator and your target component values, try adding the integrator to the PSpice model.  Run the simulation and see if it works.  Note that you will probably have to increase the gain of E2 by a factor of 10 (to 20).  If you do this in PSpice, do not forget to also add the 10(F capacitor between pins 1 and 8 of the 386 amplifier in your circuit.  Try adjusting the value of the capacitor until you get a good integration with adequate final amplitude.  [If you need to, you can use the inverting amplifier to change the gain as well.]

Adding the integrator to your circuit: After you have used PSpice to design an integrator, add the integrator to your circuit.  Don’t forget to also add any other changes you made in the PSpice model (like amplifying the signal).  Does your integrator work?  If not, rethink the values for the components you have chosen.

Take your data: When you have a working integrator, take a picture of the integrator functioning and the overall performance of the circuit and the model.  If you want in System(A-H), you can invert the output at H with the scope and with PSpice to get a better visual comparison to the input at A. No signatures necessary.

PSpice output:  Block(E-F): ______	   System(A-H): _____

Circuit with sine wave input:   Block(E-F): ______      System(A-H): _____

Circuit with audio source input:  Block(E-F): ______      System(A-H): _____

Adding a Smoothing capacitor

The final addition you will make to your circuit is to add a smoothing capacitor.

What the smoothing capacitor should do:  Recall that when you added a smoothing capacitor to the output of a rectifier, the bumps from the rectified signal were smoothed over and the output was much more even.  You can apply this concept to the signal in this circuit as well.  If we add a smoothing capacitor of the correct size, we should be able to smooth out the pulses caused by the sampling and come up with an even closer reconstruction of the original audio wave.  The figure below shows the result of adding a smoothing capacitor to the integrated signal.  It shows the original input (at point A), the output of the circuit (at point H), and the inversion of the output (at point H).  Note that the original input frequencies have been preserved, but the pulses have been largely eliminated.

What capacitance should I use?  The exact value of your smoothing capacitor will depend on your integrator and your sampling frequency.  A capacitor that is too large, will smooth over the high frequencies of your input signal.  A capacitor that is too small will not smooth over the sampling pulses.  Try experimenting with the PSpice model by adding a 1(F capacitor between point F and ground.  Look at the output.  Should the capacitance be increased or decreased?  Increase or decrease the capacitance in increments of an order of magnitude (0.001(, 0.01(, 0.1(, 1(, 10(, 100(, 1000() until you find one that gives you the best reconstruction.  You can then fine tune the capacitance using the values you have in your kit.  (For example: If you find that the range between 100( and 1000( works best, try the 330( or 220( from your kit.)  If you find you need a capacitance that you do not have, consult the staff to find out what we have available.

Check the smoothing capacitor in your circuit: Once you have decided on a good value for the smoothing capacitor using PSpice, try adding it to your circuit between point F and ground.  How does your audio output look and sound now?  If your output no longer sounds audible, or still looks very sampled, rethink the value of the capacitor.

Take your data:  Once you have decided on a good value for the smoothing capacitor that works well in both PSpice and the actual circuit, take your data.  If you want in System(A-H), you can invert the output at H with the scope and with PSpice to get a better visual comparison to the input at A.  No signature required.

PSpice output:  Block(E-F): ______	   System(A-H): _____

Circuit with sine wave input:   Block(E-F): ______      System(A-H): _____

Circuit with audio source input:  Block(E-F): ______      System(A-H): _____

Final signature:  Show a staff member the final output of your circuit.  Also demonstrate how well your circuit plays your audio signal on the speaker.

Personal Stereo _____________    Witnessed ________________

The Report

By this time, you should be familiar with the expectations of this class when it comes to  reports.  This time we are not providing you with details.  We would still like to see the same parts: introduction, background, initial design, final design, conclusions, personal responsibilities, appendices, and extra credit.  However, you will have to decide what to include in each of these sections of the report.  Since this report will be more free format than the others (in both execution on your part and grading on our part), you need not put all of your data into the appendices.  If you feel your report will be clearer with your plots and diagrams in line with the text, then put them there.  If you include them in the appendices, make sure they are clearly referenced.

When we grade your report this time, we will grade on a letter scale rather than a point scale.  This means that there will be no grading sheet and no specific point value assigned to every item you need to include in the report.  You must use your judgment as to what you feel it is necessary to include.  Use the other three reports as a guide.

The following point scale will be used:

| letter | number | +partici- pation | percent |  | letter | number | +partici- pation | percent |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A+ | 20 | 5 | 100 |  | C+ | 14.5 | 5 | 78 |
| A | 19 | 5 | 96 |  | C | 14 | 5 | 76 |
| A- | 18 | 5 | 92 |  | C- | 13 | 5 | 72 |
| B+ | 17 | 5 | 88 |  | D+ | 12 | 5 | 68 |
| B | 16 | 5 | 84 |  | D | 11 | 5 | 64 |
| B- | 15 | 5 | 80 |  | D- | 10 | 5 | 60 |