Reading assignment

Ulaby,  3-4

Connor and Salon, II-39 ( II-44

Software

div_curl_example.m

Problem 1 - Line integrals & curl

The magnetic field of a straight wire of radius a  which has a constant current density J0, is given by:

B = 0 J0 r/ 2 a 			inside the wire (r < a )

B = 0 J0 a 2/ (2 r) a 		outside the wire (r > a ).

where 0 and J0 are constants.

a.	Calculate  Bdl around the 2 paths shown in the figure below.  (The drawing shows a view as if the wire had been cut).

b.	Calculate B for both regions.

Problem 2 - Properties of fields with curl

The electric field created by a cylinder of radius a  with constant charge density 0 is:

E = 0 r / (2 0) ar 		inside the cylinder (r < a ) and

E = 0 a 2 / (2 0 r)  ar 	outside the cylinder (r > a ).

where 0 and 0 are constants.

a.	Verify that   Edl =0 on the same path as above and that E = 0.

b.	An illustration of the E and B fields can be obtained by running div_curl_example.m using matlab.  Fig. 1 is the B field while Figure 3 is the E field.  What are the properties of a field with non-zero curl?

Problem 3 - Stokes theorem

Calculate (B) ds over the surface area enclosed by the 2 paths in Problem 1 (the shaded area).  Compare your answer with the result from Problem 1a.

Problem 4 - Gradient

Compute the gradient of the following functions.

a.	f = 8 a 2 cos  + 2rz	(cylindrical)

b.	f = a   cos 2 / r 	(spherical)

Use the worksheet associated with Problem 2.8.1 in "Visual Electromagnetics for Mathcad" to check your answer.  (You may have to use a specific number instead of the variable a).

c.	Calculate f for each of the functions above.