Reading assignment

Ulaby, 4-4

Connor and Salon, I-24  I-29 and II-1  II-10

Problem 1 - Coulomb and Gauss' law

Show that the electric field of a point charge satisfies Gauss' law by evaluating

Eds over the surface of a sphere of radius a.

Problem 2 - Symmetry

Three charge distributions are pictured below.  In 1) and 3), assume that the system is very long and ignore fringe effects.   For each of the charge distributions, answer the following:

a.	Determine the direction in which E points.

b.	Determine surfaces over which Eds  is constant and non-zero.

c.	Sketch a surface that can be used with Gauss' law to find E.

Problem 3 - Use Gauss' law to evaluate E

A charge distribution with cylindrical  symmetry is shown below.  The inner cylinder has a uniform charge density v C/m3.  The outer shell has a surface charge density s C/m2 such that the total charge on the outer shell is the negative of the total charge in the inner cylinder.  Ignore end effects.

a.	Find E for r < a .

b.	Find E for a  < r < b  and for b  < r.

c.	Check your answer for E  by evaluating E and E.

d.	What is  Edl  around the contour shown on the right?

e.	Express s in terms of the geometry and v.