Reading assignment

Ulaby, 4-5

Connor and Salon, II-10  II-26

Problem 1 - Determine V from E

a.	Take the electric field from Lesson 2.2, Problem 3.   Assume that the outer cylinder is grounded.

a.	Find the voltage as a function of r for r > b  and b   > r > a .

b.	Check your result by evaluating -V.

c.	Find the voltage at r=0.

Problem 2 - Equipotential lines

Plot a set of electric field lines and equipotential lines for the quadrupole set of charges below.  Dipole equipotentials can be viewed with the Mathcad worksheet for 3.6.2.

Problem 3 - Find V from charge

a.	Find the electric potential at z = 0 as a function of r due to a line charge l that extends from z = -L/2 -> L/2.  You'll probably want to use Maple.

b.	Find the E at the same locations.

c.	When l = 10-10 C/m and L = 0.2 m, numerically evaluate V at r = 0.1 m, and E at r = 0.105 m.

d.	Approximate the line charge as a set of 4 point charges.  Calculate the voltage from the 4 point charges and compare with part c.

e.	Calculate the voltage at r = 0.11 m, and use this to estimate the electric field at r = 0.105 m.