Reading assignment

Ulaby, 4-5.5

Connor and Salon,  II-35  II-39, V-1  V-7 and V-27  V-33

Problem 1 (option 1) - analytical solution to Poisson's equation

A charged region of a semiconductor is sandwiched between two grounded conductors as shown below.

a.	Solve for V(z) by directly integrating Poisson's equation, 2V = -and applying the appropriate boundary conditions.

b.	Find E(z) and D(z).

c.	What is s on the two conductors?

Problem 1 (option 2) - analytical solution to Laplace's equation

A coaxial cable has an inner conductor (at r =a ) held at voltage V0 and an outer conductor (at r =b ) that is grounded.  There is no charge other than the surface charge on the conductors.

a.	Solve for V(r) by directly integrating Laplace's equation, 2V = 0,and applying the appropriate boundary conditions.

b.	Find E(r) and D(r).

c.	What is s on the two conductors?

d.	What is the capacitance per unit length of the cable?

Problem 2 - finite difference solution to Laplace's equation

Find the voltage at the 4 points below.

Problem 3 - Use of spreadsheet to solve Laplace's equation

a.	Use a finite difference calculation on a spreadsheet to solve for the voltage everywhere in the configuration on the left below.  The drawing illustrates the cross-section.  Assume this figure extends out of the page for a long distance.

b.	Sketch or plot the equipotentials and electric field lines.

c.	Find the charge density on the conductor at point P (0,1.5).

d.	Find the total charge per unit length on the outer and inner conductors.

e.	Determine the capacitance per unit length between the 2 conductors.