Reading assignment

Ulaby,  2-5.1, 2-5.2

Experiment 1 - Standing wave pattern - lumped line

Obtain a lumped model of a transmission line and connect it as shown.  This lumped line models an 80 meter length of RG-58 A/U coaxial cable and each L-C section has an equivalent length of 4 meters.  Set the function generator amplitude to 1 V P-P.

a.	Set ZL = 93 .

1)	Measure the voltage magnitude as a function of node number and sketch the result.  (Suggestion: first measure the even nodes, then the odd nodes).

2)	How many nodes separate Vmax and Vmin locations?  Convert your answer to an equivalent length in the coaxial line.

3)	What is Vmax/Vmin?

b.	Repeat part a. for ZL = ( ZL = 50, and ZL = 0.  To save time, you don't need to record all values.  Concentrate on finding Vmax, Vmin, and their locations.

c.	Repeat part b. with a capacitor of 3.3 nF.  What hapeens to the Vmax and Vmin locations?

d.	Run the sing_bnd.m code (Matlab file in the waves folder) which illustrates standing wave patterns.

Problem 1 - Standing wave pattern - coaxial cable

The equivalent coaxial cable circuit for Experiment 1 is shown below.  You should compare answers with the experiment wherever you can.

RG 58 coaxial cables have the following parameters:a  = 0.4 mm,b  = 1.4 mm, RC or Z0 = 50 , l = 2.5x10-7 H/m, c = 1x10-10 F/m, and r = 2.3.

a.	Determine  and the wavelength  at 1.5 MHz.  Take your measurement of the distance between Vmax and Vmin from the experiment and express in terms of .  What is the distance between two maxima?

b.	Determine the reflection coefficient at the load, L and the standing wave ratio, VSWR.

c.	Assume that the forward traveling wave has an amplitude of 1 Volt.  Sketch the standing wave pattern for voltage and current.  Include numbers for amplitudes and distances.

d.	Under what conditions do you get a voltage maximum at the load?  a minimum?

e.	If the load is a 3.3 nF capacitor, what is the reflection coefficient at the load?  Where is the location of the first minimum?

Experiment 2 - Input impedance, lumped line

Set ZL =0on the lumped line.  Examine the signal at both the input and output of the lumped line.

a.	Set the frequency to 1 kHz.  Does the input look like it is shorted?

b.	Increase the frequency to 400 kHz.  Does the input look like it is shorted?