Reading assignment

Ulaby, 6-7, 6-8

Problem 1 - Displacement current

A parallel plate capacitor with circular plates and an air dielectric has a plate radius of 5 mm and a plate separation of 10 m.  The voltage across the plates is V = 5 cos t where  = 2*100 kHz.

a.	Find D between the plates.

b.	Determine the displacement current density, (D/(t.

c.	Is there any free charge motion in the gap between the plates?

d.	Compute the total displacement current,  ( (D/(t (ds , and compare it with the capacitor current, I = C dV/dt.

e.	 What is H between the plates?