# Reading assignment

Ulaby, 7-4, 7-6.2

Connor and Salon, Unit IX

Problem  1  -  Lossy   media   parameters

Find  and  of an electromagnetic wave traveling through seawater (r = 72,  = 4 S/m) at 10 MHz and 100 GHz.

Problem  2  -  Energy  &  Power  -  lossy   media

A 10 MHz wave that is polarized in the x direction propagates in the +z direction in seawater.  At z=0, it has a power density of 10 W/m2 (Use the results of Problem 1).

a.	Write the electric and magnetic fields in phasor form.

b.	Write the electric field in time domain form.

c.	At what value of z will the power density of the wave be 1% of its initial power?