Reading assignment

Ulaby, 8-1

Connor and Salon, Unit X (On Waves & Materials)

Problem  1  -  Normal   incidence   reflection  -  conductors

A  10 GHz plane wave has an electric field magnitude of 100 V/m and propagates in the az direction through a perfect dielectric with r = 9.  E is in the ax direction.

a.	What are the incident E and H phasors?

b.	At z = 0, the wave strikes a perfect conductor.  What are the reflected E and H phasors?

c.	Use the boundary conditions to find the surface current density in the conductor.

d.	Draw the standing wave pattern for E and H (include numbers for amplitude and position).

e.	Simulate this case with sing_bnd.m by using a large imaginary dielectric for region 2.

f.	Calculate the total E and H.  (phasor & time domain form).

Problem  2  -  Normal   incidence   reflection  -  dielectrics

The same wave as in problem 1 strikes a dielectric-air boundary at z=0 as shown below.

a.	Find the reflection and transmission coefficients.

b.	What are the reflected and transmitted electric field phasors?

c.	What are the reflected and transmitted H phasors?  What is Ht/Hi?

d.	What is the standing wave ratio in the dielectric?  Sketch the standing wave pattern for E and H.  Run sing_bnd.m for this problem.

e.	What is the average power density of the incident, reflected, and transmitted waves?

Problem  3  -  Normal   incidence  -  multiple   boundaries

A  10 GHz radar transmitter is used in the configuration shown below.  Note that the radome-outside air boundary is identical to the boundary examined in Problem 2.

a.	What is |E|/|H| at the z=0 boundary of Problem 2?  (equivalent to the region 2-3 boundary in this problem).  Compare it with the value in air.

b.	Now refer to the full radome problem.  Where can you put the left boundary so that |E|/|H| in the radome matches that in the air on the left?  For mechanical reasons, the radome must be more than 2 cm thick.

c.	What is  for this value of d?

d.	What is  if d is 0.2 mm thinner than designed?